## Slide 1: ESnet’s Use of OpenFlow To Facilitate Science Data Mobility
Chin Guok
Inder Monga, and Eric Pouyoul
OGF 36 OpenFlow Workshop
Chicago, Il
Oct 8, 2012

## Slide 2: Disclaimer

## Slide 3: Pros and Cons of OpenFlow in the WAN
Separation of Control and Data Plane | 
Reduces costs | Requires infrastructure support for control plane
Simplifies operations | Control / data plane failure scenarios must be investigated for resiliency
Direct Access to Forwarding Table | 
Provides high degree of flexibility and customization | Access control to modify forwarding table is critical, concurrent access may require locks
Facilitates programmability of the network (e.g. Software Defined Networking*), and formalizes the notion of a Network OS | Reliant on third-party applications for routing functions (e.g. BGP, IGP, route / packet filtering, etc)
*NB: SDN concept has been deployed in R&E networks via dynamic circuit provisioning (e.g. IDC, NSI)

## Slide 4: OpenFlow in the WAN
Augmenting edge services*
  Facilitates moving of flows from one service (e.g. best-effort routed) to another (e.g. bandwidth guaranteed switched)
  Leveraged for monitoring / security functions
    IDS (e.g. black-holing DoS traffic)
    CALEA compliance (e.g. mirroring traffic)
Service virtualization
  Hides under-lying topology and exposes an Openflow interface for user manipulation of substrate
  Facilitates recursive partitioning of substrates
  Potential to dynamically support high layer constructs (e.g. anycast/manycast/multicast)

## Slide 5: Journey with OpenFlow/SDN Joint Techs Summer 2011, Fairbanks, Alaska
Key Features
Flexible selection of service paths
Programmatic traffic engineering
High granularity of flow separation

## Slide 6: Journey with OpenFlow/SDN Inaugural Open Network Summit, 2011, Stanford and SuperComputing 2011, Seattle
Key Features
ECSEL*: Network Control End-site to End-site IDC
Leveraging OpenFlow’s topology capabilities to dynamically learn of new connections
Coordination and orchestration of end-to-end connections at various layers
*NB: ECSEL is a modified version of OSCARS supporting end site to end site negotiation of WAN resources, and on the fly LAN provisioning using OpenFlow

## Slide 7: OneSwitch*: Abstracting the topology. Giving control to the application
Virtual OpenFlow Switch
Application
Controller
Key Features
Virtualizes a WAN substrate/slice as a single switch
Allows for recursive abstraction of slices
Exposes programmatic OpenFlow interface to user
Target as SC12 demonstration
*NB: This effort is funded as a DOE ASCR research project
Notes: ***Explain – One Switch and how it hides the physical topology
Virtual Switch makes it possible to view the entire ESnet as a single switch , with each of the
edge Openflow switches being represented as switch ports. With this abstraction ,
the application controller just has to send flow mod to Virtual Switch telling it to forward the
packet from one switch port to another. Simple , is nt it !!!

## Slide 8: Implementing the ScienceDMZ Design Pattern
Simple application of OF
OF Switch: fine grained mapping of science flows to guaranteed bandwidth circuits
  Dynamic
  Application/Policy driven
  Automated VLAN translation
OF Controller: manage WAN resources (virtual circuits, bandwidth etc.)
  Site administrative resource allocation
  Site-WAN, Site-Site policies enforced
OF Switch
DTNs
Border Router
WAN
OSCARS
virtual circuits
(L2 VLANs)
OF
Controller

## Slide 9: Additional Thoughts
With the distinct separation of control and data plan functions, resiliency is a vital consideration when deploying OpenFlow in the WAN
  Google leverages the distributed computing model and pre-computes failure scenarios to recover from failures
Having control plane functions done out-of-skin by 3rd party software (i.e. different from network device vendor), requires appropriate support models to be in place
  Google develops and supports (in-house) the OpenFlow deployment in it’s internal WAN backbone
OpenFlow formalizes the concept of the Network OS by defining network device primitives (i.e south-bound interface to devices), the Network OS north-bound is yet to be determined and must be carefully considered
  There are several potential candidates for the north-bound interface, e.g. OGF NSI, NOX programmatic interface, OpenStack Quantum, etc

## Slide 10: Questions?