## Slide 1: SwitchingService (SS)
Takahiro Miyamoto
KDDI R&D Laboratories Inc.

## Slide 2: SwitchingService (NSI-SS)
Be a new NSI service to realize multipoint network.
Introduce a new endpoint called Switching Point (SP).
Only NSI-CS
NSI-CS with NSI-SS
STP:X:B/v1
Network Y
STP:X:E/v3
STP:X:D/v1
STP:X:C/v1
STP:Y:F/v1
STP:Y:G/v1
STP:Y:H/v1
Network X
NG
STP:X:B/v1
Network Y
STP:X:E/v3
STP:X:D/v1
STP:X:C/v1
STP:Y:F/v1
STP:Y:G/v1
STP:Y:H/v1
Network X
STP:Y:S.A/v1
STP:Y:S.B/v1
STP:Y:S.C/v1
SP:U:S
OK

## Slide 3: Relationship between NSI-CS and NSI-SS
Requester
Provider
crt.rq
crt.cf
rsv.rq
rsv.cf
term.rq
term.cf
del.rq
del.cf
NSI-SS process
NSI-SS process
NSI-CS process
SP
STP
virtual STP
create/delete SwitchingPoint add/remove virtual STPs
Connect between STPs
SwitchingService (SS)
ConnectionService (CS)

## Slide 4: Definitions
SwitchingPoint (SP)
  SP has multiple virtual STPs.
  SP acts as non-blocking.
  A Requester agent can create multiple SPs in a domain.
Virtual STP
  Virtual STP belongs to a SP.
  Virtual STP does not need to map physical network equipment.
  Virtual STP is exchanged via only NSI-SS.
  Virtual STP is not published via Topology Service.
SP
STP
virtual STP

## Slide 5: Operations
create
  Create a new SwitchingPoint (SP).
addSTP
  Add new virtual STPs in an existing SP.
removeSTP
  Remove existing virtual STPs from an existing SP.
delete
  Delete an existing SP and its virtual STPs.
query
  Retrieve SPs and virtual STPs.

## Slide 6: create() operation
Requests a new SwitchingPoint.
  globalSwitchingId and switchingId are assigned by a Requester.
    They are similar to globalReservationId and connectionId, respectively.
  The number of Virtual STP is specified by the Requester.
Ethernet
IP (multicast)
OpenFlow
enum
UUID
UUID

## Slide 7: create() confirm response
Returns virtual STP list which is assigned for the Requester.
  The Requester can reserve a connection between STP described in topology and the virtual STP.
Equal to StpType defined in NSI-CS

## Slide 8: create() fail response
Returns Exception.
Equal to ServiceExceptionType defined in NSI-CS

## Slide 9: addSTP() operation
Requests new virtual STPs in a specified SP.
  SwitchingCapability (Ethernet or OpenFlow) can not be changed.

## Slide 10: addSTP() confirm response
Returns added virtual STP list which is assigned for the Requester.
  Existing virtual STPs are not included.
Equal to StpType defined in NSI-CS

## Slide 11: addSTP() fail response
Returns Exception.
Equal to ServiceExceptionType defined in NSI-CS

## Slide 12: removeSTP() operation
Requests to remove an existing virtual STPs in a specified SP.

## Slide 13: removeSTP() confirm response
Returns confirmation only.

## Slide 14: removeSTP() fail response
Returns Exception.
Equal to ServiceExceptionType defined in NSI-CS

## Slide 15: delete() operation
Requests to remove a SP and an virtual STPs in the SP.

## Slide 16: delete() confirm response
Returns confirmation only.

## Slide 17: delete() fail response
Returns Exception.
Equal to ServiceExceptionType defined in NSI-CS

## Slide 18: query() operation
Requests to get existing SPs.
Request can filter on switchingId and globalSwitchingId.

## Slide 19: query() confirm response
Returns SP information.
  switchingId
  virtual STP list
  state (active / inactive)

## Slide 20: query() fail response
Returns Exception.
Equal to ServiceExceptionType defined in NSI-CS

## Slide 21: Example Create() request contents
<create>
<switchingId>urn:uuid:deb6aa8d-3e59-4821-9f7f-5c808be42bde</switchingId>
<criteria>
<switchingCapability>Ethernet</switchingCapability>
<serviceAttributes>
<attribute type="vlan" targetNamespace="http://schemas.ogf.org/nml/ethernet/2013/10/#">1701</attribute>
</serviceAttributes>
</criteria>
<stpCount>2</stpCount>
</create>
SwitchingId assigned by a Requester
SwitchingCapability
Ethernet parameter
Required virtual STP count

## Slide 22: Example Create() response contents
<createConfirmed>
<switchingId>urn:uuid:deb6aa8d-3e59-4821-9f7f-5c808be42bde</switchingId>
<stpList>
<stp>
<networkId>urn:uuid:kddilabs.jp</networkId>
<localId>urn:uuid:deb6aa8d-3e59-4821-9f7f-5c808be42bde/1</localId>
</stp>
<stp>
<networkId>urn:uuid:kddilabs.jp</networkId>
<localId>urn:uuid:deb6aa8d-3e59-4821-9f7f-5c808be42bde/2</localId>
</stp>
</stpList>
</createConfirmed>
SwitchingId assigned by a Requester
virtual STPs