## Slide 1: NSI implementation plan of G-lambda
Atsuko Takefusa and Tomohiro Kudoh,
National Institute of Advanced Industrial Science and Technology (AIST)
http://www.g-lambda.net/

## Slide 2: G- lambda project overview
Joint collaboration project of KDDI R&D labs., NTT, NICT and AIST.
G-lambda project has been started in December 2004.
The goal of this project is to establish a common web services interface (GNS-WSI) between Grid resource manager and network resource manager.
Draft specification of GNS-WSI3 is available at:
  http://www.g-lambda.net/

## Slide 3: G-lambda’s plan to implement NSI
G-lambda is a collaboration to define an interface
  Implementation of GNS-WSI has been carried out by AIST, NTT and KDDI R&D labs. Independently
  We have three implementations of GNS-WSI3
AIST, KDDI R&D labs. and NTT will implement NSI independently
  AIST implementation will be (partly) ready by GLIF Rio
  KDDI implementation may be ready by GLIF Rio
  NTT will implement NSI by SC11
NTT has a plan to use NSI at SC11 demonstration
  Graphical simulation of measurement-based path selection
  Application-driven global path switchover without packet loss
    (Switches over to better path, according to the performance fluctuation)

## Slide 4: AIST will implement NSI as proxies to GNS-WSI
Key differences between GNS-WSI and NSI
  GNS-WSI has a factory service which creates a SM for each reservation
    In NSI, there is no explicit such service. A SM is created when a reservation request is received.
  GNS-WSI does not support repetitive provision/release
    Provisioned at the start time
    De-provisioned at the end time or a cancel message
  GNS-WSI supports auto-start only
    No manual provisioning
  GNS-WSI supports two-phase commit
    Commit of a reservation is required before auto-provisioning
    Assumes timeout in a certain period of time

## Slide 5: NSI and G-lambda GNS-WSI (GL) Proxies
Implement NSI-GL Proxy and GL-NSI Proxy
NSI-GL Proxy invokes "create" before "reserve"
GL supports NSI provision and release
  NSI_provision, NSI_release
Coexistence of manual (NSI) and auto (NSI/GL) provisioning
  Add "NSI = true" option as a reservation attribute
    If NSI == true, proxy waits "provision"
    Otherwise, proxy invokes "provision" immediately after commit
1PC (NSI) and 2PC (GL) conversion

## Slide 6: NSI-GL Proxy

## Slide 7: GL-NSI Proxy

## Slide 8: Demo scenarios