## Slide 1: NSI-based experiment plan for optical path network and topology description
Tomohiro Kudoh
(AIST)

## Slide 2: Victories project and its network model
Vertically Integrated Center for Technologies of Optical Routing toward Ideal Energy Savings (VICTORIES) was established in 2008 within AIST
Aims to produce a dynamic optical path network technology that can realize a huge throughput with a significantly lower power consumption.
Experiment and demonstration planned in Oct. 2014.
In the experiment, extended-NSI will be used for resource management of network and other resources.

## Slide 3: Dynamic node
Multi-layer network node consists of:
  Fiber cross-connect switch
  Wavelength selective switches
  ODU switches
  Ethernet switches

## Slide 4: Experimentation topology

## Slide 5: A dynamic node
App.
E-SW
And
Trans.
Opt.
SW
WSS
TPA
d
d
d
d
NSA
(uPA)
d
VOD-SA
: network
Northbound I/F:
NSI
Northbound I/F:
NSI + VOD-SD

## Slide 6: Resource management model of VoD application
DC
Sub.
VOD-SA
NSA
VOD-SA
NRM
VoD
Coordinator
Resource
Aggregator
Contents archive
Opt. path NW
Opt. path NW
VoD Servers
DC
③deploy contents
④Deliver
Resource
database
NW provider
NW provider
①request
②resource rsv.
Res. Usage
history
User
database
Monitoring
★Resource discovery
We will use NSI framework for both network and video service resources

## Slide 7: Service plane overview
VoD requester (tablet)
Resource Coordinator
(Aggregator）
Contents DB
NSI Aggregator
NSI/VOD
Aggregator
NSI uPA
NSI uPA
B: VOD-Server
A: archive
C: VoD client
Path Finder
VOD-SA
VOD-SA
UG
UG

## Slide 8: Topology description
Topology consists of:
  Topology
  Constraints definitions

## Slide 9: Schematic description of topology
Schematic CAD for digital circuits is used
  KiCAD eeschema (GPL v2 licensed)
    Hierarchical design is supported
  Developed Python script to convert KiCAD native netlist to topology descripition in JSON format.

## Slide 10: Device description
"urn:ogf:network:victories_demo:2014:_Dnode1_WXC4X4V_1": {
"address": "192.168.1.23", # NSA address
"constrain": "constraininfo.json#WXC4X4", # pointer to constraints info
"exchangeCapable": ["ODU"], # label swapping capability class
"ports": { # start of port descriptions
"1": {
"name": "urn:ogf:network:victories_demo:2014:_Dnode1_WXC4X4V_1_IO1",
"protocol": "ANY",
"type": "LAMBDA"
},
--- snip ---
"10": {
"name": "urn:ogf:network:victories_demo:2014:_Dnode1_WXC4X4V_1_AD2",
"protocol": "ANY",
"type": "LAMBDA"
},
}
}

## Slide 11: SDP (net) description
"$118": { # net_id, (an id of SDP, used internally)
"_attribute_": {
"Delay": [
350.5
],
“OpticalPower": [
-6.5
],
"media": "SMF",
},
"urn:ogf:network:victories_demo:2014:_Dnode5_FXC16V_2": 4,
"urn:ogf:network:victories_demo:2014:_Dnode6_FXC8V_1": 1
},

## Slide 12: Network and its constraint description
Network is described as a “device” in schematic CAD
Each “device” is associated with a constraint description

## Slide 13: Constraints: connectivity
Internal connectivity matrix（✔: can be connected）
Constraint description
"AvailableConnections" : {
  "ColumnIndex" : [1, 2, 3, 4, 5, 6, 7, 8 ],
  "1" : [1, 2, 3, 4, 5, 6, 7, 8 ],
  "2" : [1, 2, 3, 4, 5, 6, 7, 8 ],
  "3" : [1, 2, 3, 4, 5, 6, 7, 8 ],
  "4" : [1, 2, 3, 4, 5, 6, 7, 8 ],
  "5" : [1, 2, 3, 4 ],
  "6" : [1, 2, 3, 4 ],
  "7" : [1, 2, 3, 4 ],
  "8" : [1, 2, 3, 4 ]
  }
 | IO1 | IO2 | IO3 | IO4 | AD1 | AD2 | AD3 | AD4
IO1 | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
IO2 | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
IO3 | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
IO4 | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
AD1 | ✔ | ✔ | ✔ | ✔ |  |  |  | 
AD2 | ✔ | ✔ | ✔ | ✔ |  |  |  | 
AD3 | ✔ | ✔ | ✔ | ✔ |  |  |  | 
AD4 | ✔ | ✔ | ✔ | ✔ |  |  |  | 

## Slide 14: Constraints: labels
Optical Add Drop Multiplexer (OADM)
"AvailablChannels" : {
  "1" : "1-32",
  "2" : "1-32",
  "3" : "1-32",
  "4" : "1-32",
  "5" : "1-32",
  "6" : "1-32",
  "7" : "1-32",
  "8" : "1-32"
  }
"MaximumChannels" : {
  "1" : 32,
  "2" : 32,
  "3" : 32,
  "4" : 32,
  "5" : 1,
  "6" : 1,
  "7" : 1,
  "8" : 1
  }
Port 1 IN
Port 2 IN
Port 3 IN
Port 4 IN
Port 1 OUT
Port 2 OUT
Port 3 OUT
Port 4 OUT
Port 5 IN
Port 6 IN
Port 7 IN
Port 8 IN
Port 5 OUT
Port 6 OUT
Port 7 OUT
Port 8 OUT

## Slide 15: Protection Capability
"Protectable" : true,
"ProtectablePorts" : [5, 6],
"ActiveSystemPorts" : [1, 2, 3, 4],
"StandbySystemPorts" : [1, 2, 3, 4]
1
2
3
4
5
6
protected port
active port
standby port

## Slide 16: Gain and OSNR
"Gain" : {
  "ColumnIndex" : [1, 2, 3, 4, 5, 6, 7, 8 ],
  "1" : [-7.0, -7.0, -7.0, -7.0, -7.0, -7.0, -7.0, -7.0],
  "2" : [-7.0, -7.0, -7.0, -7.0, -7.0, -7.0, -7.0, -7.0],
  "3" : [-7.0, -7.0, -7.0, -7.0, -7.0, -7.0, -7.0, -7.0],
  "4" : [-7.0, -7.0, -7.0, -7.0, -7.0, -7.0, -7.0, -7.0],
  "5" : [-7.0, -7.0, -7.0, -7.0, null, null, null, null],
  "6" : [-7.0, -7.0, -7.0, -7.0, null, null, null, null],
  "7" : [-7.0, -7.0, -7.0, -7.0, null, null, null, null],
  "8" : [-7.0, -7.0, -7.0, -7.0, null, null, null, null]
  }
"OSNR" : {
  "ColumnIndex" : [1, 2, 3, 4, 5, 6, 7, 8 ],
  "1" : [2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3],
  "2" : [2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3], "3" : [2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3], "4" : [2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3], "5" : [2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, null, null, null, null],
  "6" : [2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, null, null, null, null],
  "7" : [2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, null, null, null, null],
  "8" : [2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, null, null, null, null]
  }

## Slide 17: An example constraint description
"WXC4X4" : {
"Comment" : "Combination of TPA and WSS consists a WXC",
"NumberOfPort" : 8,
"AvailableConnections" : {
  "ColumnIndex" : [1, 2, 3, 4, 5, 6, 7, 8 ],
  "1" : [1, 2, 3, 4, 5, 6, 7, 8 ],
  <SNIP>
  "8" : [1, 2, 3, 4 ]
  },
"AvailablChannels" : {
  "1" : "1-32",
  <SNIP>
  "8" : "1-32"
  },
"MaximumChannels" : {
  "1" : 32,
  <SNIP>
  "8" : 1
  },
"Protectable" : true,
"ProtectablePorts" : [5],
"ActiveSystemPorts" : [1, 2, 3, 4],
"StandbySystemPorts" : [1, 2, 3, 4],
"Gain" : {
  "ColumnIndex" : [1, 2, 3, 4, 5, 6, 7, 8 ],
  "1" : [-7.0, -7.0, -7.0, -7.0, -7.0, -7.0, -7.0, -7.0],
  <SNIP>
  "8" : [-7.0, -7.0, -7.0, -7.0, null, null, null, null]
  },
"OSNR" : {
  "ColumnIndex" : [1, 2, 3, 4, 5, 6, 7, 8 ],
  "1" : [2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3],
  <SNIP>
  "8" : [2.2E-3, 2.2E-3, 2.2E-3, 2.2E-3, null, null, null, null]
  }
  }