## Slide 1: Service Definitions
A feature proposed for NSI version 2.0

## Slide 2: Problem:
As the technologies in our networks varies considerably from domain to domain, how do reconcile the needs of the “requestor” with the capabilities of the “provider”?
  Not all capabilities are present in every network
  Providers cannot guarantee every aspect of a hardware technology as a service feature…
  Requesters cannot be expected to know details of every technology in every domain in order to specifiy their configuration.
  There is no common adoption of terms and quantification of provisioning or transport details.
We need a mechansim to bound the characteristics of a Service so that providers know *exactly* what they are committing to provide…-> so that they can allocate the resources, tools, and skills sets to guarantee the service features..
We need a means to express these service capabilities to users (and other automated agents) so that they can pose requests that can be honored.
In a guaranteed performance world, we need a means of clearly stating what is “required” (by the RA) and what is “committed to” (from the PA).

## Slide 3: Service Definition
“Service Definitions” were conceived to provide a formal mechanism to declare and bound the range of service characteristics associated with a Connection Service
  This allows providers to guaranty the service capabilities they express in a Service Definition, and
  This allows users to discern exactly what service capabilities they can request – with the expectation that these capabilities will be guaranteed.
A comprehensive service “specification” covers a broad range of aspects associated with a service offering
  These may include AAI profiles, help desk, monitoring, accounting, etc.
For this OGF NSI v2.0 discussion, we are only interested in those technical aspects that are a specific part of the protocol or the topology that are necessary to express service capabilities of NSI domains.
These are refered to as “Service Definitions”

## Slide 4: The Basic “Service Definition”
The Service Definition consists of a set of characteristics, or “service parameters”, that identify and bound salient aspects of the service
  Examples: “bandwidth”, or “bit error rate”…
Since the final arbiter of a service parameter’s meaning is the network engineer or the code developer, these service parameters should therefore have a human readable form that Is unequivocal in its meaning.
For each service parameter, there is more formal specification of a range/set of values that the service provider is prepared to accept in a Reservation Request as technically viable and is prepared to guarantee if confirmed.

## Slide 5: Service Parameters
Parameter | Range | Units | Human description
BW | 0 to 10^10 | Bits per second | Bandwidth. This is the requested Bandwidth of the connection. The provided Bandwidth shall not vary more than +-.1% when measured over any 10 second period.
FER | 10^-8 | Frames | Frame Errorr Rate. This is the number errorred frames per second
MBS | 72 |  | Maximum Burst Size. This is the maximum number of bits that can be ingressed at wire speed per second
MTU | 1500 or 9280 | Bytes | Maximum frame size the service can transport intact.
PreserveIFG | False |  | The inter-frame gap is not preserved in this service. Therefore the user can not rely on ingress flow pacing/shaping to be preserved end to end.

## Slide 6: Service Parameters
Thus these service parameters make up the formal set of characteristics that govern a service
  All aspects of a service that constitute part of the service guaranty are identified by a service parameter
  Any aspect not identified by a service parameter is explicitly undefined. I.e. there is no valid assumption that can be made regarding presence or predictability of such mythical characteristics.
These Service Parameters completely bound the service capabilities that a PA is responsible for delivering.
In general, services parameters should be describing aspects of the service, not aspects of hardware. The intent is to allow the local network engineering and management decide how best to deliver the advertised services

## Slide 7: Service Definition Example
<serviceDefinition name=“DXQ” >
<serviceDescription>
    Ethernet framed data transport. This service constructs Connections that transport data found in the payload section of an 802.1Q ethernet frame. STPs in this service are mapped to IEEE 802.1Q tagged ethernet packets. format. The 802.1Q PDU frame itself is not considered transport payload, just the payload contents. Inter-frame spacing is explicitly NOT preserved.
</serviceDescription>
<serviceParameters>
<Bits-per-second units=“bits per second” >
from 0 to 10000000000 units bits
</Bits-per-second>
<Max-Frame-Size units=“bytes”> 1500 or 9280 <Max-Frame-Size>
<Max-Burst-Size units=“bytes”> 100000 <Max-Burst-Size>
</serviceParameters>
<serviceDefinition>

## Slide 8: Creating a Service Definition
Anyone can define any NSI Connection Service SD simply by formally defining the parameter space their service recognizes.
A network can offer a particular Connection Service by engineering it’s internal infrastructure and the internal NRM to honor the parameters of the SD.
The SD for a service domain can be announced in several possible ways:
  It can be stored as a web doc and the URL is included in the public topology announcement for that network.
  The SD specification itself can be directly included in the Network block of the topology announcement. (thus simplifying access to it.)
These discovery mechanisms allow the SD to flow thru the network via topology (which is a natural association.)

## Slide 9: “Common Service Definitions”
Several networks may conspire together to define a single “common service definition” which they all agree to implement.
  This insures compatibility and interoperability among the services end to end.
Example:
  NetA SD:
    BW := 0 to 10^10 bps /* 10 Gbps */
    MTU := 9280 bytes default=9280
  NetB SD:
    Bandwidth := 0 to 10^11 bps /* 100 gbps */
    FER := 10^-8 default=10^-8
  Common SD:
    CSD_type = AutoGOLE-SD
    Capacity:= 0 to 10^11 units=bps
    MTU := 9300 units=bytes default=9300
    MaxFER := 10^-8 to 0 default 10^8

## Slide 10: Service Definitions and CS Protocol
The Service Definition identifies the parameters that bound a particular service.
i.e. A NSI-CS ReservationRequest() must fall within these parametric bounds
Thus, the SD service parameters also form the request parameters:
  Explicit declarative parameters (parameters that have only one possible value are assumed to be that value and can be, but need not be, present in the Resv request.
  Parameters that express a set or range of values may have a default value. These parameters must be either explicitly specified in the request, or the default value is used. If a required parameter is missing, and no default is specified in the SD, the request is rejected.
Example:
Resv( src=A:A1; dst=C:C2; start=today@15:00; end=start+12:00;
Auth=foo@nordu.net blah blah;
CSD_type=AutoGOLE-SD; capacity=10^9; )
the MTU and MaxFER paramters are missing from the request, but have defaults defined in the SD.

## Slide 11: Service Definitions and CS Protocol
The NSI Framework poses several attributes of any “Connection”, and therefore of all Connection Services.
  These base Connection attributes are:
    Source STP, and Destination STP
    Schedule (start time, end time)
    Policy (who can do what)
    Performance (what are the technical capabilities required.)
The Service Definition is relevant to all of these, but the most complex and the most variable is the Performance guarantees
  I propose we focus on these aspects initially as the most crucial to be resolved.
  We can formally define protocol fields for the NSI “Base” parameters, and have a separate section for “Service Specific” parameters.

## Slide 12
The CSD (or “SD”) defines the “template” for a service request – it identifies the parameters that must be specified in order for the Provider to fullfil the request.
The Reservation carries a similar a Service Request (“SR”) “form” which is essentially a set of parameters taken from the SD and defined as desired by the Requester within the bounds of the SD.
Since some parameters may be delegated to the PA to ‘fill in the blanks’, the Reservation response must contain a Service Confirmation (“SC”) form containing the “as-built” information – the SD template fully filled out.

## Slide 13: Service Termination Points
STPs identify the topological location where the connection service payload is exchanged with external networks.
Payload
  “Payload” is the information that is carried transparently end to end, unmodified, by the associated NSI Connection instance.
Access Framing
  The “access framing” is the formatting information or other control/wire information ->at the STP <- that separates “payload” from “not payload”.
  Framing information may also be a component that separates one STP from another, e.g. 802.1Q frames contain a VLANID that differentiates Service Termination Points within a particular ethernet flow.
  Payload must be presented at the egress STP in a fashion that as much as possible preserves the “unmodified” aspects of the user data flow.

## Slide 14: Service Termination Points
Simple initial proposition: All STPs for a particular service definition type are the same.
  Heterogeneous STPs introduce significant complexities into the the NSI Connection abstraction
  Example: Take a NSI Network service that contains STPs that map to ethernet or Sonet..
Homogeneous STPs provide a simple initial services model that will allow us to develop basic path finding processes, topology constructs, and real performance engineering/provisioning techniques.
  Heterogeneous STPs are not precluded, but these pose complexities that are not easily resolved (yet). We can re-visit more complex topological issues later.

## Slide 15: Service Termination Points
Mapping the STP
  The STP represents a connection endpoint. Thus, the ingress STP must mapTo a n-tuple that fully and uniquely identifies the input payload.
  Similarly, the egress STP must map to a similar n-tuple to properly deliver the payload where the client expects to see it.
  Thus, within a mulitplexed or virtualized flow of packets/frames that are associated with different connections, the STP may identify the payloads from any possible set of identifying characteristics – they need not be simply from the “framing” data.
  For example, we could define an STP to be 802.1q frames with vlan 100 carrying IP packets with TCP port 80. And then claim the entire ethernet PDU as the payload. To be fair, we cannot redirect such a packet to, say, a different vlan as this would violate payload immutability. But we could switch the flow to another port.
  (This seems a bit esoteric, but in fact is a very powerful aspect of STPs that will prove useful in the future… This is an advanced topic…)
How STPs are identified is a function of the NSI Service with which they are associated. i.e. STP specifications are part of the Service Definition.
  The STP mapping is not carried in the NSI protocol, (since the framework is technology agnostic) so

## Slide 16: AutoGOLE Service Definition DXQ
Potential : DXQ
Service Type: Data Transport for 802.1Q framed payloads
    Abreviation: DXQ
  Description: User data in the payload data section of an 802.1Q ethernet frame is carried from the ingress STP to the egress STP.
  STP specification:
    All STPs mapTo a tuple that uniquely identifies a flow of IEEE 802.1Q frames with a specific VLAN ID on a specific physical interface port.
    In DXQ, the Ethernet frame (PDU) itself is not considered part of the payload, though a particular DXQ service provider may elect to carry the frame along with the payload.
    Specifically, 802.3 untagged frames and 802.1ad (QinQ) dual tagged frames are disallowed as STPs in DXQ version 1.0 (these are special cases and need further consideration before including them in the SD.)

## Slide 17: AutoGOLE DXQ
Proposal #1: DXQ
  Since the .1Q ingress PDU is not part of the payload, the network(s) are free to modify the framing along the path, as long as the payload is again presented as the payload data section of an 802.1Q frame at the egress point.
  Thus, the payload may be presented at the egress point in a .1Q frame that has a different VLAN tag than the ingress point, i.e. the service is allowed to perform VLAN rewrite/translation/swapping.

## Slide 18: AutoGOLE Service Definition ETS
Alternative Proposal #2: EVTS
  Service Type: Ethernet VLAN Transport Service
    Abreviation: EVTS
  Description: The payload data is the ethernet PDU in its entirety. The EVTS service transports “ethernet frames” associated with a particular VLAN from an ingress point to an egress point. This is in effect a tunnel over which 802.1q frames are blindly carried.
    Since the entire frame is considered the Payload, no modification of the frame is allowed. Thus, the sum result is that no VLAN swapping is allowed – and so clients can be assured that the VLAN tag presented at the ingress will not be changed in transit and the packet will appear at the egress on the same VLAN.
  STP specification:
    For EVTS v1.0 all STPs map to a tuple that uniquely identify a flow of 802.1q frames with a specific VLAN ID.
  Note: While this SD tells you the VLANs can not (will not) be swapped, it does not tell you which STPs correspond to the same VLAN ID. A port adjacentcy matrix (could express this…or VLAN planes could do so.

## Slide 19: AutoGOLE Service Definition ETS
Alternative Proposal #2: EVTS
  This service does not “build a VLAN” across networks. EVTS constructs a point to point connection that carries tagged frames from ingress to egress. Note: An EVTS service provider may elect to build a VLAN across the transport infrastructure to deliver the service payload, but this is not required or recommended and may have undesirable consequences for both the network and the user payload.
  The EVTS service provider should also be wary of mapping such flows to 802.1ad (QinQ) flows as these insert an additional VLAN tag in the payload frame thus modifying the payload. This has an effect on the MTU limits for the flow and the Frame Check Sum value that must be recomputed. Fundamentally, this breaks payload immutability and should be avoided – though in reality it may have only limited impact on real users.
  It is recommended that EVTS connections be encapsulated inside another technology in order to preserve payload immutability. Such techniques may employ 802.1ah (Provider Based Bridging), MPLS LSPs, GFP/SONET-SDH, or other isolation techniques.

## Slide 20: Service Definitions and STPs -
NetB
SD=EVTS
802.1Q PDU
User Data Section
NetA
SD=DXQ
NetC
SD=DXQ
vl=4
Vl=99
Vl=99
Vl=6
stp C:C2
mapsTo:
sw=x1.edu
p=ge0/2/3
vl=6
stp C:C1
mapsTo:
sw=x1.edu
p=ge0/2/3
unit=99
C1
C2
B2
A2
A1
B1
Stp B:B1
mapsTo:
sw=chi-a
pic=2/0
if=0
vl=99
Stp B:B2
mapsTo:
sw=cph1
p=ge-3-4.99
Stp A:A1
mapsTo:
<12><4>
Stp A:A2
mapsTo:
<10><99>
PDU is the payload
Transport framing could be…EoMPLS?

## Slide 21: Mixing Services
Both DXQ and EVTS define similar STPs.
  This is fine. Indeed, both services may announce STPs that have exactly the same physical mappings – but this is not intriniscally obvious or germane to Requesting Agents.
  A request to DXQ service can offer vlan swapping capability.
  A request to EVTS would deliver a flat VLAN connection.
  Both services could co-exist if necessary…

## Slide 22: Other considerations
“PA Only” NSAs pose problems in that their service puts constraints (bounds) on even the base parameters – specifically the Source and Destination STPs.
  But there is no existing mechanism to announce this fact…and so requests that are not completely local will be rejected.
A Service Definition that explicitly bounded the STPs that could be used in a Reservation would indicate this anolmaly
Example SD parameters:
<serviceDefinition>
<sourceSTP> ES.net.EVTS:* </sourceSTP>
<destSTP> ES.net.EVTS:* </destSTP>
</serviceDefinition>
This requires a more sophisticated parser, but such a function will likely be used for enumeration and pt-to-anypt specifications as well.

## Slide 23: Considerations
The wide range of variability of parameters and their values makes specification of a SD schema difficult – the schema elements must be able to reflect almost any type of value…
  This also limits the useful ness of a structured data format as it becomes difficult to validat any particular aspect of the resulting SD instance.
This requires more exploration – by an XSD type expert…

## Slide 24: Consideration
These configurable Service Definitions allow us to tailor services to our community’s needs
They also provide a clear engineering target for engineering teams.
Without this service orientation, we will require many hard-coded service parameters
  These will vary by hardware capabilities….

## Slide 25: Recomendations
The Service Definition concept is gaining acceptance in many R&E networks as a well organized approach to formal service specification. We should adopt it and smooth out the rough spots – and automate it.
Can we agree to include Service Definitions as a V2.0 feature ?
  Specifics TBD but following the basic concepts as outlined herein.