## Slide 1: NSI Interoperability Plugfest
GLIF Summer 2011
Rio de Janiero, BR
Sep 13, 2011
Jerry Sobieski
NORDUnet

## Slide 2: What is the NSI Plugfest?
NSI := The OGF “Network Service Interface” specification
  A framework for a scalable inter-domain service architecture, not just a signaling protocol.
  And the Connection Service (NSI-CS) protocol doc, a technology agnostic protocol for provisioning connections across
The NSI Plugfest is a demonstration of progress towards deployable software incorporating the NSI CS protocol and framework.
The objective is to demonstrate the interoperable CS protocol developed independently by multiple organizations
  Interoperability
  Identify flaws and/or inconsistencies
  Identify missing pieces necessary for full fledged services

## Slide 3: Who is participating?
We have 7 NSI-CS v1.0 implementations:
  OpenNSA (NORUnet)
  AutoBAHN (GEANT)
  DRAC (SURFnet)
  G-LAMBDA (AIST)
  G-LAMBDA (KDDI Labs)
  OSCARS (ESnet)
  DynamicKL (KISTI)

## Slide 4: How is the Plugfest organized?
We have defined 4 “Challenges” for each NSI implementation to complete:
  #1: Self consistent messaging and lifecycle
      Make sure your NSA can talk to itself and successfully sequence a connection though the life cycle.
  #2: Cross-NSA messaging and lifecycle
      Show that your NSA dn other NSAs interpret messaging in the same way through the lifecycle.
  #3: Multi-domain segmentation
      Demonstrate the ability to successful segment and reserve a multiple domain service request, again managing connection through the entire lifecycle.
  #4: Query information access
      Exercise the authorized access to the NSI service tree information associated with a multi-domain connection.

## Slide 5: Plugfest Topology
For the initial NSI protocol testing that is Rio Plugfest, we elected to use an artificial topology:
This is the “Rio” ring topology.
Each NSA is allowed to define their internal topology as they see fit as long as it is consistent with this inter-domain view.
A1
A2
A3
A4
B1
B2
B3
B4
C1
C2
C3
C4
D1
D2
D3
D4
J2
J3
J4
J1
Jamaica
Aruba
Bonaire
Martinique
Grenada
Dominica
M1
M2
M3
M4
G2
G4
G3
G1
OpenNSA
DRAC
AutoBAHN
OSCARS
G-LAMBDA/AIST
G-LAMBDA/KDDIL
DynamicKL
Curacao

## Slide 6: The Challenge #3
C
G
C
J
Leaf NSAs
NSI Client (application)
Aggregating NSA

## Slide 7: Plugfest Topology
With the collaborative efforts of the NSI WG, the GLIF DToX TF, and the Automated GOLE project, we were able to take existing technology and adapt it to fit NSI Topology model for the Plugfest.
  We are using the RDF based OWL data description language to capture the topology elements and their relationships.
  And we have used the SNE graphical topology editor to input most of the topo information.
  Thanks to the UvA team for the SNE + OWL/RDF and the DToX folks for their flexibility when it came to modifying their topology to meet the NSI needs.
For Rio, we manually construct a global topology view and make it available to each NSA for testing.
The Plugfest topology approach is a hack done for a demo. It lacks a number of important features before we can view it as a long term answer.
  Topology will be the next key topic for the NSI Working Group

## Slide 8: Plugfest Status
The NSI implementations are assumed to have completed Challenge #1 – the ability to converse with themselves to manage a connection.
Nearly all have completed Challenge #2 – meaning they have worked out the low level message transport issues and basic content issues that were not clear from the spec or that exposed bugs in software or libraries.
We have successfully demonstrated a Challenge #3 reservation request:
  Aruba -> Granada -> Dominica
  (OpenNSA) (GLAMBDA-AIST) (OSCARS)
  Caveat: The whole life cycle needs testing.
We have partial results on Challenge #4 – simple queries are working in several NSAs.

## Slide 9: Challenge #1 & #2 Matrix
https://docs.google.com/document/d/1McNO8NP2bXGjgJTk4hsPDARL-NehXEP_I4eNJZE93tM/edit?hl=en

## Slide 10: Results: A snippet of NSI CS
2011-09-12 22:34:32.429 +0900 INFO finish auto commit of Coallocator-0912133102-COMMAND-32-for-Coallocator-0912133102-RESERVE-32
2011-09-12 22:34:32.468 +0900 INFO end provisionBeforeStart for connId=urn:uuid:ed811582-dd43-11e0-83ff-00144f20a8d2
2011-09-12 22:34:32.468 +0900 INFO Change State: RESERVED -> AUTO_PROVISION, connId=urn:uuid:ed811582-dd43-11e0-83ff-00144f20a8d2
2011-09-12 22:36:54.714 +0900 WARN nsi.checkSessionSecurityis true, but missing SessionSecurityAttr in the received request. Allow it just for demo!
2011-09-12 22:36:54.715 +0900 INFO Change State: INITIAL -> RESERVING, connId=urn:uuid:43914672-dd44-11e0-a711-00144f20a8d2
2011-09-12 22:36:54.715 +0900 INFO start reservation for connId=urn:uuid:43914672-dd44-11e0-a711-00144f20a8d2
2011-09-12 22:36:54.716 +0900 INFO
[ReservationRequestType received]
CorrelationId urn:uuid:43914b9a-dd44-11e0-a711-00144f20a8d2
replyTo http://orval.grid.aau.dk:7080/NSI/services/ConnectionService
RequesterNSA urn:ogf:network:nsa:Aruba-OpenNSA
ProviderNSA urn:ogf:network:nsa:Grenada-GLAMBDA-AIST
sessionSecurityAttr null
GlobalReservationId urn:uuid:43913f92-dd44-11e0-a711-00144f20a8d2
description Test Connection
ConnectionId urn:uuid:43914672-dd44-11e0-a711-00144f20a8d2
ServiceParams
Schedule
start Mon Sep 12 13:40:43 GMT+00:00 2011
end Mon Sep 12 13:45:43 GMT+00:00 2011
duration null
Bandwidth
Desired 1000
Minimum null
Maximum null
Path
direction BIDIRECTIONAL
srcSTP
stpId urn:ogf:network:stp:Grenada:G1
stpSpecAttrs null
stpList null
destSTP
stpId urn:ogf:network:stp:Grenada:G3
stpSpecAttrs null
2011-09-12 22:36:54.716 +0900 INFO start Glambda create for connId=urn:uuid:43914672-dd44-11e0-a711-00144f20a8d2
2011-09-12 22:36:54.739 +0900 INFO start Glambda reserve for connId=urn:uuid:43914672-dd44-11e0-a711-00144f20a8d2
2011-09-12 22:36:54.763 +0900 INFO start Glambda waitCommandStatus(PREPARED) for connId=urn:uuid:43914672-dd44-11e0-a711-00144f20a8d2
G-LAMBDA AIST Log: http://163.220.30.174:8090/logs/nsi_gl_proxy.log
Reservation request
NSAs
End points of the connection

## Slide 11: Issues and Lessons Learned
Topology is critical, and
    A more thoroughly comprehensive and standardized NSI Topology model is required.
    A distributed topology management scheme is necessary
    Better integration with local topology is necessary.
Several hacks appeared in the WSDL as result of adhoc optimizations/mods not [currently] part of the standard:
    Separate contact information for PA functions of the NSA and the RA functions of the NSA. This continues to cause considerable confusion.
    Use of SOAP and replyTo to route NSI message sequencing…
Several message elements need review – the spec was clear, but the implementation revealed functional layer violations
    Header fields requesterNSA/providerNSA
    Some surprises in message serialization (race conditions)
Many important features were disabled in order to show message exchange and basic processing
    Ex: Secure messaging, resource allocation, hardware interfaces, information elements within messages, etc.
Service definitions need to be carefully designed and engineered in the field to take advantage of the NSI automation capabilities.
[even simple] Interdomain PathFinders are [still] lacking…

## Slide 12
New Endorsements – NSI is gaining very broad support.
I once made a connection this long using NSI v1.0

## Slide 13: Next up: Supercomputing
The Automated GOLE project plans a demo using NSI CS v1.0 across real infrastructure for SC2011 (Nov 2011, Seattle)
    ~8 weeks from now!!
Things we need:
    Full life cycle processes for all participating NSAs
    Functioning NRMs integrated with the NSA, and covering real GOLE hardware
    A viable “service definition” that is engineered in each GOLE to be compatible and consistent with NSI framework and CS protocol
    CS v1.0 errata

## Slide 14: Come see NSI at GLIF Rio !!
The NSI development/interop/demo will be running continuously during the GLIF conference
Please wander through at your convenience and inquire about the progress…

## Slide 15
Plugfest Issues:
  Henrik Thostrup Jensen (NORDUnet – OpenNSA)
  John MacAuley (SURFnet – DRAC)
  Tomohiro Kudoh (GLAMBDA – AIST)
  Jerry Sobieski (NORDUnet)
  Radek Krzywania (PSNC – AutoBAHN)

## Slide 16: Radek
- ConnectionStateType.TERMINATEING - maybe TERMINATING looks better
- GenericAcknowledgmentType - should xxxConfirmed/Failed messages be sent before returning this type, or asynchronously? It could be removed as well
- queryConfirmed, queryFailed on provider interface - breaks consistency
- query on requester interface - breaks consistency
- maybe allow suggestion that either chain or tree reservation model is prefered in reservation request
- reservation name is inconsistence with other method names (should be reserve, or change terminate to termination)
- xxxConfirmed/Failed - all take some common parameters but wrapped into diffrent types, so more writing required instead of having one method to set this field, i.e.: ReservationFailedRequestType reqFail = new ReservationFailedRequestType(); reqFail.setCorrelationId(correlationId); reqFail.setReservationFailed(createFailed(conState, messageId, text)); and ProvisionConfirmedRequestType reqConf = new ProvisionConfirmedRequestType(); reqConf.setCorrelationId(correlationId); reqConf.setProvisionConfirmed(createConfirmed()); in both cases (and it applies for other methods) ReservationFailedRequestType and ProvisionConfirmedRequestType same fields are carried, one common type would save writing
- We experienced from the demo, that sending a provision request just after reservation request, results in simple ack. So in fact we are unaware if the reservation is in auto provision state or not. We just get provisioned status update when reservation start time comes. We can wait 1 minute for that during demo, but if the service is about to start in 4 weeks...
- People were asking for query message, to retrieve the reservation status at all partners and a path.
- People were also interested if the same path will be configured for each provision message
- protocol does not specify it, it’s actually up to domain, but in some cases it may be important (see Express scenario later)
- Express was also interested in specyfing path for the reservation. E.g. they have one reservation now, and another in two months - two reservations needs to go the same path. We can't solve it now.
Express also experienced issues with any connections they get - they need to tune it before use. Sa they do that about 2 weeks before operations, and check again about 1 day or hours before sending data. This scenario is a real user scenario, which we should discuss. I've invited the guy (apology - I forgot his name, but I will find him at the venue during break) from Express for the March OGF meeting in Oxford so we could discuss it.

## Slide 17: Henrik
This was intended for some post-Rio dissemination: Things which are confusing people: - The URN prefixes - Requester / provider role fields - ReplyTo - Distributed development - Bad error messages from SOAP/WSDL stacks (and probably other things as well) - Reordering of messages from "logical order" - XML/WSDL namespaces What did work: - Deadlines makes people do work - Having developers in chatroom

## Slide 18: Henrik
Protocol:
The schedule has a start time, end time and duration. - AFAICT we do not need duration. Can anyone explain what we need it for?
Is there a rationale for the minimum and maximum bandwidth? (I entered the NSI community a bit late, so humor me).
The callback model makes it very non obvious to handle failures. - In general, dealing with network problems has not been thought through. - This becames fairly clear when we had problems establishing connection. There is nothing specified on how to continue from there (i.e., who carries the responsibility for propagating state updates).
The TechnologySpecificAttributes does not seem to have any usage, except "future compatability", but are there no examples or use cases for them. - I suggest removal, and then adding specific fields if we need them later.
The reservationConfirmed message includes all the reservation details. Is this really necessary? Couldn't it just be a simple acknowledgement.
I would consider adding a state to indicate that the connection failed for some reason. The terminated state is a bit broad in what it describes.
Having two ways of querying seems like one too many. Remember that both have to implemented. Is there a reason we cannot just have one?
The term "NsiExceptionType" seem to have gotten into the spec. It should be called serviceException.
The messageId in the serviceException should either have a number of options or not be there. - It should probably be called errorId as well (it doesn't identify a message). - A possiblity could be to adopt the HTTP error codes.
The text and variables solution in serviceException seems like overkill. Why not just have the text there?
Quite often it is not clear what fields are required in a message and which are not.
WSDL:
XML Schema has a value "Terminateing" for ConnectionState.
xsd:dateTime allows value without a timezone, which is problematic. - I suggest that the protocol dictates that all protocol timestamps should be in zulu time (which is really the only sensible thing to send over a wire IMHO)
WSDL specifies a reservation.reservation, which is somewhat unfortunate. I suggestion reservation.reservationInfo
connectionId is enforced as a UUID, which is not tune with the protocol spec. which specifies that the connectionId only has to be unique within the requester NSA scope.
ServiceException should probably be called "serviceException" to follow the naming convention.

## Slide 19: Henrik
I've also compiled a list of issues which have been confusing people. The purpose of this list is simply have a spec which is easy(er) to implement, which IMHO is very important quality of standard (and one we are far from).
- The URN prefixes
- Requester / provider role fields - replyTo / addressing in general - Distributed development - Reordering of messages from "logical order" - Bad error messages from SOAP/WSDL stacks (and probably other things as well) - XML/WSDL namespaces - Security I have some comments/suggestions as well: The URN prefixes are just prefixes. They do not add any value, and have been a source of confusion. I suggest we remove them. I'm not sure the requester/provider role fields are really necessary. It should be clear from the security context (I'll get back to that), who it is one is communicating with. The replyTo fields seems to me like being a surrogate for dealing with lack of addressing for not having topology done. On the other hand they also make it a lot easier to make clients as a client does not have to exist in the topology to be able to comminicate with an NSA. I suggest we think a bit over how we want this to work, and how we want to support potentially short-lived clients creating connections (because something needs to initiate connection creation). The distributed collaboration with developing NSI agents was initally a bit fuzzy and hindered by some barriers. The skype room improved this a lot by bringing down the latency in developer communication. Reordering of messages from "logical order". I still think the protocol design is a bit clumsy, especially when combined with the lack of how to handle network errors (unavailable hosts, etc.) and short-lived clients. I've been thinking a bit about it, but haven't really come up with any substantial. Some people (me included, if not especially) have struggled quite a bit with their SOAP/WSDL stacks, and the lack of checks and bugs in there. However several people have also been puzzled with the error messages from them .e.g., getting an integer parsing error when an element was simply missing. Somewhat similar, I had an issue where my SOAP stack used the wrong namespace on an element. The issue here was no so much the bug in the SOAP stack (it happens), but that I could not figure out what was right and wrong by looking at the WSDLs. Security. Let me be very clear here. HTTP basic and some SAML attributes have nothing to with security. It did not provide integrity, confidentiality, or assurance. I am also puzzled by the choice of SAML, as SAML is intended for communication between identity providers and services, but there are no identity providers in NSI. Also, I don't think that anyone in this group actually understands SAML (I don't). My suggestion for security is to use TLS with certificates (from a recognized CA) in each end, and nothing more. It is not the most trivial thing in the world (but isn't really difficult either), but it fairly well understood and has widespread support. Lastly, I think the group is suffering heavily from having thought too much and having constructued to little. This has of somewhat changed after Rio, but I fear that we are now so far into the process with writing the standard, that it is difficult to have any big changes done, as people do not want to change what has already been made. The project group also still operates in very ad-hoc fashion. This can work great to a certain extent, but I think that limit has been crossed some time ago. We need to get better organized, but this is not really my area of expertise, so I won't suggest something.

## Slide 20: MacAuley
The reservation XML message contains two element tags both named “reservation”. The first is the reservation operation and the second is the reservation information contents. This will need to be fixed in the types XSD.
The “providerNSA” and “requesterNSA” elements in the NSI protocol header caused some confusion. In the CS document we stated that this would be populated with the NSnetwork URN as defined in Salt Lake City. However, when the demo topology schema was created we introduced a new NSA object. Some people used the URN of the NSA object in the “providerNSA” and “requesterNSA” elements. We will need to make a definitive statement as we define the formal NSI topology. Do we rename the elements to “providerNSnetwork” and “requesterNSnetwork” and continue using the NSnetwork URNs, or do we switch over to NSA URN?
Demo topology definition was an issue, but in the end we had something workable for the demo. Going forward we need to formalize NSI topology definition and how it relates to other schema such as DTOX and NML. I am going to start working on the topology discovery/exchange problem to get use moving forward.
Security presented interoperability issues as some people enforced authentication and authorization while others did not. Some systems could not provide the needed credentials, and resulted in some incompatibility. I believe we are clear on what we want to implement for NSA-to-NSA security, but we need to formalize the session security requirements so we can begin to implement in the NSAs.
Namespace issues – this is not an issue with the protocol specification but with a few of the less mature SOAP web services toolkits. They get confused between the interface and type namespaces for the protocol elements due to the use of “ref” to reference protocol operation elements from the types XSD in the interfaces WSDL.
Now that we have had some demo experience with error handling, I think it is time to start formalizing values in the NsiExceptionType. I have already identified ten generic error conditions, and I am sure there are many more.
As a follow up to this item, NSA implementations need to populate the NsiExceptionType.variables with additional information to help identify the problem that caused the rejection of the message. I had done this in OpenDRAC so any errors returned to other NSA would contain information formatted as follows: <messageId>SVC0001</messageId> <text>Invalid or missing parameter</text> <variables> <Attribute Name="replyTo" NameFormat="urn:oasis:names:tc:SAML:2.0:attrname-format:basic"> <AttributeValue xsi:type="xs:string" xmlns:xs="http://www.w3.org/2001/XMLSchema" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" >&lt;null&gt;</AttributeValue> </Attribute> </variables>
Interface version discovery – I had discussed this with the group previously, but now that we are moving forward, up issuing NSI schema versions, and adding new interfaces we will need a mechanism for discovering the interfaces and versions supported by an NSA. I will propose something formal when I get a chance.

## Slide 21: Tomohiro
1. WSDL provisioning
  While some clients (AIST and KDDI) tried to get WSDL from servers before establishing a session, some servers did not provide WSDL. This problem was solved by make AIST and KDDI implementations to read local WSDL, but we are not sure whether using a local WSDL is right thing or not.
2. Lessons learned (?) - Ack and conf/fail sequence problem. AIST implemented processing of request such as reserve as a different thread from the one which receives requests. Therefore, a confirm message is sometimes returned before the ack. But some implementations did not allow it. (this problem has not been fixed yet) - We experienced network problems (like connection refused), especially between OpenNSA and others. The ack and conf/fail sequence matter may be the cause of these network problems . But not quite sure. This should be investigated further. - Implementations used different timezones in specifying times. One of the implementations worked only if a reservation request is made in the same timezone. Also, using different timezones for logs is not very human understandable.
2. SAML We don't think the discussion on SAML is mature enough. At this moment, we should not put SAML security attributes in the WSDL. Extensible specification can be used for future extension (including SAML) like : <xsd:any namespace="##other" processContents="lax" minOccurs="0" maxOccurs="unbounded"/> Just as an example, OGF OGSA-BES (Basic Execution Service) does not include security attributes in WSDL or schema, and uses xsd:any multiple times so that outer schema can be used for security attributes.
3. synchronous/asynchronous call It seems using a separate session for confirm/fail is confusing. We have to introduce correlation id, and also we encountered a problem in the order of ack and confirm messages as stated above. Asynchronous calls are now widely used for many services, and supported by most of toolkits including Axis, CXF, Glassfish and Websphere. A major advantage of asynchronous call is that the client can be at behind a NAT. On the other hand, since a connection is there until a reply is sent back, there is a limit in the number of requests which have not been replied. But (especially if we will modify the protocol to reply to provision request in Autostart immediately), there will not be so many connections at a time. We are not proposing this for v1.0, but we think it should be considered (again) for v2.0.
4. WSDL related - The STP list is defined in WSDL as: <xsd:complexType name="OrderedServiceTerminationPointType"> <xsd:sequence> <xsd:element name="stpId" type="tns:StpIdType" /> </xsd:sequence> <xsd:attribute name="order" type="xsd:integer" /> </xsd:complexType> But <order> is not necessary. Order of array elements are guaranteed in both JAXB and SOAP. Same for DetailedPathType. - xsd:integer can be xsd:int xsd:integer is mapped to BigInteger in Java. Normal xsd:int would be sufficient.

## Slide 22: Jerry
Header fields - rename the requesterNSA and providerNSA in the NSI msg.
ACK vs Response.
Serialization of pairwise messaging.
strict separation of MTL layer from NSI layer
May need an MTL interface and processing description.
Redefine the STP to be a tuple of <stp> <NSnetwork><localid></stp> So that the NSI network relationship is explicit in the structure of the object, not simply assumed by the name of the STP. This is a topology issue.
Do we really need URNs for topology components? The protocol does not need URNs as network names. or local id names. The current scheme overlays topology into the naming scheme requiring parsing of the name…this is should be avoided.
“Standards process” vs “coding” - This effort is not a proof of concept…This is an interop of the standard as is. New ideas not already explicitly defined in the spec should go first to the working group for open discussion, concensus, and documentation. Never insert “expected”, “anticipated”, or “optimization features” into the standard. The WSDL is part of that standard and *EVERYTHING* that goes into the WSDL should be understood and agreed to by the group before it is accepted. THat measn ideas need to be placed on the weekly call agenda for presentation and discussion. Not simply inserted to see who screams.
Restraint in proposing new protocol features and tweeks... The NSI protocol is one of the most powerful protocols I've seen in the last 15 years for doing what it does. There is very little it cannot do within the current specification - much of the recent “cool” ideas are simply attempts to replicate some existing feature of a previous tool...Resist it! We have a new model with a well considered set of comprehensive primitives. We may require new mechanisms for doing things we want to do…we should not assume conventional processes are necessary in a future facining architecture.
Don't be tempted to believe a cute little feature doesn't have significant impact of both the functional architecture, as well as the complexity and communicates a sense of scatter shot design by knowlwedgeable folks we want to adopt the protocol and framework.
Fix State Machine to return provision response always immediately...don't wait until the provision completes.
Topology - we need to address a more NSI model, and a consensus specification.

## Slide 23: Jerry
Worked well:
  The Skype NSI-WG list
  The plugfest “Challenge” structure
  Graphically defining topology
    SNE editor was good proof of concept…but needs some enhancement/bug fixes:
      Does not work consistently in different browsers
      The graphical user interface was klunky beyond a small topology…
  The RDF/OWL data description was useful and seemed to not be easily integrated by coders