## Slide 1: Connection Versions in v2

## Slide 2: Don’t Panic!
What you are about to see is a behaviour model – not a required software design.
  It only poses internal structure as an example!

## Slide 3: Diagramatical terms
NSA
NSA
NSA
NSA
NSA
“Local” NSA
“Originating” NSA
3-level service tree model
“Children” agents
RA
PA
RA
RA
PA
PA
PA
RA

## Slide 4: Basic Information Model
Every Connection Instance has a set of “versions” associated with it
  Version numbers are integer values, 0 (zero) or greater
  The version number is optionally assigned by the RA in the Reserve.rq() – even for the initial reservation.
  Subsequent Reserve.rq version numbers may be specified by the RA in a monotonically increasing manner (they need not be sequential.)
  If the version is blank/missing/empty in the Reserve request, the PA will return an error.

## Slide 5: Basic Information Model
Upon receiving a syntactically valid Reservation request, a PA assigns a ConnectionID to the request, and constructs [internally] a “Primary Connection Information Block” (“PCIB”) associated with that ConnectionID
  The PCIB contains of an open ended chain (or list) of “Connection Version Blocks” (CVs)
  Each version block holds the constraints requested by the originating RA for that connection version.
  Each version block contains a chain (or list) of Connection Segment Blocks that define the children for that version
  The CSB elements represent the “RA”s for the children
Children associated with different versions need not be the same

## Slide 6: Data organization for “Local NSA”
PCIB CID=“p1”
Vers=(n)
Orig RA info
SegID#1,v(i)
RA info
PA info
...
Vers=(m)
Orig RA info
Vers=(q)
Orig RA info
SegID#2,v(i)
RA info
PA info
SegID#3,v(i)
RA info
PA info
SegID#1,v(j)
RA info
PA info
SegID#4
RA info
PA info
SegID#3
RA info
PA info
SegID#1,v(k)
RA info
PA info
SegID#5
RA info
PA info
SegID#4
RA info
PA info
SegID#3
RA info
PA info
SegID#5
RA info
PA info
...
Children
Segments
Primary Connection Information Block – includes
The Connection ID assigned by the local NSA
Connection
Versions

## Slide 7: What can be modified
In general and by protocol, any parameter of an existing Connection may be modified.
Specific individual service implementations may restrict which parameters they will allow to be modified.
  The Service Definitions can indicate if a service attribute is “modifiable”.
  For example, the ETS service definition can indicate that only “end time’ and “capacity” can be modified.

## Slide 8: Points and open issues...
  The PA must track the highest successfully reserved version, lowest active version, and current (active) version numbers for each connection
  On a Reserve Fail, only the reservation version that failed is canceled.
  A failed version number can be reused. (yes)
    A one-time use rule could easily be implemented, and would uniquely identify modify attempts for forensic purposes...
  Can we terminate (cancel) a particular version (?)
    Yes. If we can fail a reserve.rq by version#, we also require ability to terminate by version# to clean up other children.
    This is done with an “Abort()” primitive.
    Implemented as: terminate <*> or terminate <v#>

## Slide 9: Points and open issues...
Resource tracking must differentiate the versions
  I.e. if a resource becomes unavailable, the ConnectionID and version that is affected must be identifiable.
  Transitions (Commit.rq?) from one version to another is “hitless”...
    Hitless requirements cannot be more strict than the scope of acceptable error rates for a particular service.” (Identified in the Service Definition.)
      i.e. all circuits have an acceptable error rate.
    Hitless does *not* mean without detectable implications to the data flow...
      To quote LHCONE: “Hitless means we don’t want TCP sessions to fail due to a modification.” (Harvey Neuman)
      Using the LHCONE criteria – a modification could pose a significant albeit temporary hiccup in the data flow and still be acceptable.

## Slide 10: Points and Other Issues...
  What happens if a reserve.rq is applied to an existing version (?)
    Should the specified version be interpretted the “current” connection to be modified and a new version# generated?
    Or is this to be interpretted to “please reserve the resources specified in this version”
    This is a semantic error that the RA specified version# is already in existance. The Reserve.rq is failed with appropriate error.
  A rollback could solve non-deterministic state issue. Use the “commit.rq <vers#>” to commit an earlier version.
    If we have the information...why could we not simply commit (re-configure) a prior v#
    No roll-back in NSI-CSv2.

## Slide 11: Aging out versions
Deleting historical version info locally does not mean that version is no longer in effect end-to-end.
Retaining deprecated version info can be useful
  It is very cheap (the data is already present, simply hold it until the the entire Connection is cancel.)
  Can provide operational visibility for forensics
An NSA MUST retain version details for all versions that have or will have active segments (These are “relevant” versions)
An NSA MAY retain version details of historical (non-relevant) Connection versions

## Slide 12: APAN Daejeong – NSI Tutorial

## Slide 13: The Tutorial details (so far)
Asia Pacific Advanced Networks organization
  Meeting at KISTI (?) August 19th
We have been requested to do a reprise of the GLIF NSI Tutorial presented in Hawaii in January
  This was one day
  Oriented towards Network engineers (not applications developers per se)
  Hands on exercises
    Installing and configuring NSAs
    Constructing networks among switches

## Slide 14: Help is needed
This tutorial should reflect the latest NSI protocols: CSv2, DSv1, TS? ...