## Slide 1: Thoughts on the Firewall NAT issue*
Tomohiro Kudoh
* I think the issue we are discussing as the “firewall issue” is almost a NAT issue (i.e. a process is not accessible using a global IP address). “Firewall” implies a lot of functionality and if there are non-NAT firewall issues they should be considered case by case basis.

## Slide 2: At where do NAT issues exist?
At a client/uRA
  Clients are likely to be at behind NATs.
  It will be beneficial to make a client NAT friendly.
At an aggregator/uPA
  Aggregators and uPAs provide services to clients/NSAs. It is natural that they have a global IP address.
  (If an operator should place an aggregator / a uPA behind a NAT, they should use a conventional method to make a punch hole.)

## Slide 3: Some ways to go avoid the NAT issue
Use of a NAT traversal scheme
Use Polling. Requester polls status of provider periodically.
Keep a connection initiated by a requester, for future messages sent from the provider.

## Slide 4: Relationship with MTL
Relationship of NAT issue and MTL is basically an implementation matter.

## Slide 5: Coordinator and Message Transport Layer (MTL)
Coor is a part of NSI stack, and uses MTL to send/receive messages
Coor is primarily responsible for keeping track of messaging state, e.g.
  Who was the message sent to
  Was the message received (i.e. ack’ed or MTL timeout)
  Who has not replied to the message (e.g. *.cf, *.fl, etc)
MTL is primarily responsible for sending and receiving messages, and notifying Coor if the message was received, or if a (MTL) timeout occurs
MTL interface (to Coor) has 2 simple operations:
  Send: waits for ack to be returned by destination MTL, or timeout happens. Timeout value is implementation dependent. NB: The MTL may be implemented to retry sending messages, but this is opaque to the Coor
  Receive: a thread in Coor is invoked when a message is received
NSA
NSI Stack
Message Transport Layer
Coordinator
Recall MTL interface; Chin’s slide

## Slide 6: Option A: MTL hides NAT issues
Method 1, 2 or 3 is implemented under MTL I/F.
MTL I/F layer supports MTL’s two simple operations (send/receive)
NAT support layer supports communication over NAT.
(True) MTL (like SOAP, http, TCP) exists under NAT support layer
NSA
NSI Stack
(True) Message Transport Layer
Coordinator
NAT support layer
(Method 1,2 or 3)
(fake) MTL I/F layer

## Slide 7: Option B: over-NAT communication is supported by the Coordinagtor
Method 1, 2 or 3 is implemented under MTL I/F.
MTL I/F layer supports MTL’s two simple operations (send/receive)
NAT support layer supports communication over NAT.
(True) MTL (like SOAP, http, TCP) exists under NAT support layer
NSA
NSI Stack
Message Transport Layer
Coordinator
NAT support layer
(Method 1,2 or 3)

## Slide 8: Example: JAX-WS-based asynchronous operations
JAX-WS-based asynchronous operation keeps a connection for a long period of time until a reply is sent back.
Define waitStatus as a JAX-WS-based asynchronous operations, instead of polling-based getStatus
  Reduce the number of getStatus operations
  Can respond as soon as status has changed
Requester
Provider
getStatus
Not_ready
getStatus
Reply
Reply ready
interval
Requester
Provider
waitStatus(“Reply")
Reply
Reply ready
Polling-based approach
Asynchronous approach