## Slide 1: A hierarchical, NSI compatible, topology proposal for NML
Jerry Sobieski
NORDUnet
Presented at OGF 34

## Slide 2: Hierarchical topology…
The existing NSI topology model does not provide a consistent mechanism for exposing intra-domain topological structure.
  The base model hides all internal structure…which is good in many (most) high level cases…. But…
  Where a network wishes to do so, it should be able to expose additional internal structure or state in a measured and graduated degree…down to the hardware minutia if so desired.

## Slide 3: NML recommendations
This proposal retains the NSI abstractions at the highest topological layer,
and retains the NSI model internally as smaller NSI domains are defined
A key relation called an “alias” is defined to link STPs (NML Ports) at any desired level to STPs at the next lower (more detailed) level.
  An Alias is an internal topological construct that should probably be stored at the lower level (more detailed level).
  It therefore stays private until/unless that level is announced externally. (local agents will not have a problem using this relation.)
An Alias could [alternatively] reference a conventional NML topological object – thus mapping the NSI topology to appropriate NML object as the local topology manager deems appropriate.

## Slide 4: NSI Topology Example Current existing NSI topology model: only L0 has structure, L1+ is opaque (private)
PSNC
Topo level 1
NetherLight
Topo level 1
Internet2
Topo level 1
NDN.EFDX
Opaque internal
Topo level 1
Universal space
Topo level 0
NetherLight-o
Internet2
Pionier
ION-o
NDN
NDN
NDN
SDPs (NML Links)
STPs (NML Ports)

## Slide 5: Proposed Hierarchical NSI Topology Example Proposed NorthernLight topology: L0 & internal L1 objects are publically announced by NorthernLight; As a Worldview, this topo would say I2, PSNC, and NL only announced L0 information. As a Local Topology from NDN, this is the only L0 information that NorthernLight can provide (i.e. its direct adjacencies)
Pionier
Topo level 1
NetherLight
Topo level 1
Internet2
Topo level 1
NDN.EFDX
Topo level 1
Universal space
Topo level 0
NYC Level 2
CPH
Level 2
NetherLight
Internet2
Pionier
NYC
AMS
POZ
NDN
CPH
ION
NDN
NDN
Blue links are “aliases” indicating an level transition in the topology. (Aliases act similarly to SDPs, so red and blue relations are simple logical links.)

## Slide 6: Hierarchical Topology Proposal Bi-directional Example
topo{ name $L0$; /* level 0 is the universal space */
topo{ name NDN.EFDX; version 2012-02-29-18:42:23 /* level 1 topology */
NSA https://orval.grid.aau.dk:9443/NSI/services/ConnectionService
port Pionier, NetherLight, Internet2 bidirectional;
topo{ name CPH; location lat 24.1234 lon -57.2345; /* level 2 topology */
port AMS, POZ, NYC bidirectional;
}
topo{ name NYC; location lat 24.1234 lon -87.2345; /* level 2 topology */
port ION, CPH bidirectional;
}
link NYC:CPH, CPH:NYC; /* level 2 to level 2 */
alias NDN.EFDX:Pionier, CPH:POZ; /* level 1 to level 2 boundary links */
alias NDN.EFDX:NetherLight, CPH:AMS; /* level 1 to level 2 boundary links */
alias NDN.EFDX:Internet2, NYC:ION; /* level 1 to level 2 boundary links */
}
Link NDN.EFDX:Pionier, Pionier.EFDX:NDN; /* NDN level 1 port to Pionier level 1 port */
Link NDN.EFDX:NetherLight, NetherLight.EFDX:NDN; /* level 1 port to level 1 port */
Link NDN.EFDX:Internet2, Internet2.EFDX:NDN; /* level 1 port to level 1 port */
}

## Slide 7: Modular description
network $L0${ /* level 0 is the top level universal space */
has_networks NDN.EDFX, Pionier.EFDX, NetherLight.EFDX, Internet2.EFDX;
link CPH:POZ, Pionier.EFDX:NDN; /* SDP */
link CPH:AMS, NetherLight.EFDX:NDN; /* SDP */
link NYC.ION:Internet2, Internet2.EFDX:NDN; /* SDP */
}
network NDN.EDFX { ; version 2012-02-29-18:42:23 /* level 1 network */
NSA https://orval.grid.aau.dk:9443/NSI/services/ConnectionService;
has_networks CPH, NYC;
port CPH:POZ, CPH:AMS, NYC:ION bidirectional; /* STPs */
link NYC:CPH, CPH:NYC; /* SDP */
}
network Pionier.EFDX {
NSA https://.....
port Pionier.EFDX:NDN;
}
network NetherLight.EFDX {...}
network Internet2.EFDX {...}
network CPH { ; location lat 24.1234 lon -57.2345; /* level 2 network */
port CPH:AMS, CPH:POZ, CPH:NYC bidirectional; /* STPs */
}
network NYC { ; location lat 24.1234 lon -87.2345; /* level 2 network */
port NYC:ION, NYC:CPH bidirectional; /* STPs */
}
Proposal by T.K.

## Slide 8: Modular description / network view
network $L0${ /* level 0 is the top level universal space */
has_networks NDN.EDFX, Pionier.EFDX, NetherLight.EFDX, Internet2.EFDX;
}
network NDN.EDFX { ; version 2012-02-29-18:42:23 /* level 1 network */
NSA https://orval.grid.aau.dk:9443/NSI/services/ConnectionService;
has_networks CPH, NYC;
port CPH:POZ, CPH:AMS, NYC:ION bidirectional; /* STPs */
link CPH:POZ, Pionier.EFDX:NDN; /* SDP */
link CPH:AMS, NetherLight.EFDX:NDN; /* SDP */
link NYC.ION:Internet2, Internet2.EFDX:NDN; /* SDP */
}
network Pionier.EFDX {
NSA https://.....
port Pionier.EFDX:NDN;
link Pionier.EFDX:NDN, CPH:POZ; /* SDP */
}
network NetherLight.EFDX {...}
network Internet2.EFDX {...}
network CPH { ; location lat 24.1234 lon -57.2345; /* level 2 network */
port CPH:AMS, CPH:POZ, CPH:NYC bidirectional; /* STPs */
link CPH:NYC, NYC:CPH; /* SDP */
}
network NYC { ; location lat 24.1234 lon -87.2345; /* level 2 network */
port NYC:ION, NYC:CPH bidirectional; /* STPs */
link NYC:CPH, CPH:NYC; /* SDP */
}
Proposal by T.K.

## Slide 9: Modular description / with alias
network $L0${ /* level 0 is the top level universal space */
has_networks NDN.EDFX, Pionier.EFDX, NetherLight.EFDX, Internet2.EFDX;
}
network NDN.EDFX { ; version 2012-02-29-18:42:23 /* level 1 network */
NSA https://orval.grid.aau.dk:9443/NSI/services/ConnectionService;
has_networks CPH, NYC;
port CPH:POZ alias NDN.EDFX:Pionier , CPH:AMS alias NDN.EDFX:NetherLight, NYC:ION alias NDN.EDFX:Internet2 bidirectional; /* STPs */
link NDN.EFDX:Pionier, Pionier.EFDX:NDN; /* SDP */
link NDN.EFDX:NetherLight, NetherLight.EFDX:NDN; /* SDP */
link NDN.EFDX:Internet2, Internet2.EFDX:NDN; /* SDP */
}
network Pionier.EFDX {
NSA https://.....
port Pionier.EFDX:NDN;
link Pionier.EFDX:NDN, NDN.EFDX:Pionier; /* SDP */
}
network NetherLight.EFDX {...}
network Internet2.EFDX {...}
network CPH { ; location lat 24.1234 lon -57.2345; /* level 2 network */
port CPH:AMS, CPH:POZ, CPH:NYC bidirectional; /* STPs */
link CPH:NYC, NYC:CPH; /* SDP */
}
network NYC { ; location lat 24.1234 lon -87.2345; /* level 2 network */
port NYC:ION, NYC:CPH bidirectional; /* STPs */
link NYC:CPH, CPH:NYC; /* SDP */
}
Proposal by T.K.

## Slide 10: Modular description / no internals
network $L0${ /* level 0 is the top level universal space */
has_networks NDN.EDFX, Pionier.EFDX, NetherLight.EFDX, Internet2.EFDX;
}
network NDN.EDFX { ; version 2012-02-29-18:42:23 /* level 1 network */
NSA https://orval.grid.aau.dk:9443/NSI/services/ConnectionService;
port NDN.EDFX:Pionier , NDN.EDFX:NetherLight, NDN.EDFX:Internet2 bidirectional; /* STPs */
link NDN.EFDX:Pionier, Pionier.EFDX:NDN; /* SDP */
link NDN.EFDX:NetherLight, NetherLight.EFDX:NDN; /* SDP */
link NDN.EFDX:Internet2, Internet2.EFDX:NDN; /* SDP */
}
network Pionier.EFDX {
NSA https://.....
port Pionier.EFDX:NDN;
link Pionier.EFDX:NDN, NDN.EFDX:Pionier; /* SDP */
}
network NetherLight.EFDX {...}
network Internet2.EFDX {...}
Proposal by T.K.