## Slide 1: NSI Implementation Task Force
NSI protocol and the dreaded firewall
John MacAuley

## Slide 2: The Firewall Problem
Firewall
NSA A
Requester
NSA B
Provider
ReserveRequest
ReserveConfirmed
“NSA A” behind firewall issues HTTP ReserveRequest to “NSA B” on the public network.
“NSA A” populates private IP address into replyTo field for response.
Firewall NATs HTTP request and passes on to “NSA B” but does not NAT the private IP address since this is embedded in the SOAP message.
“NSA B” cannot reach the private IP address to deliver the ReserveConfirmed message.
Private IP address
Public IP address

## Slide 3: It Gets Worse
Firewall
NSA A
NSA B
ReserveRequest
The problem exists even when public IP addresses are assigned to an NSA behind a firewall, if that firewall is blocking HTTP requests.
Public IP address
Public IP address

## Slide 4: Pathological Case
Firewall
NSA A
NSA B
ReserveRequest
“NSA A” cannot reach “NSA B” behind the firewall to issue request.
“NSA B” cannot reach “NSA A” behind the firewall to issue request.
Public IP address
Public IP address
Firewall
ReserveRequest

## Slide 5: Proper Configuration of Firewall
Firewall
NSA A
NSA B
ReserveConfirm
For NSA with public IP addresses behind the firewall:
  Access control lists can be set for peer NSA in combination with port filtering to allow an NSA behind a firewall to have traffic to it’s HTTP server port passed through.
Public IP address
Public IP address
Firewall
ReserveRequest

## Slide 6: Proper Configuration of Firewall
Firewall
NSA A
NSA B
ReserveConfirm
For NSA with private IP addresses behind the firewall:
  Firewall will need to act as public entity for NSA.
  Access control lists can be set for peer NSA in combination with NAT and port forwarding to allow the requesting NSA to be mapped through to the provider NSA’s HTTP server port within the DMZ
  A requesting NSA behind a firewall will need to provide the public facing IP address and port of the firewall within the replyTo field of the SOAP request.
Private IP address
Private IP address
Firewall
ReserveRequest
Public IP address
Public IP address

## Slide 7: Summary
Provider NSA must be publically accessible
  Must have publically accessible interface to receive request messages from Requester NSA.
Requester NSA must also be publically accessible
  Must have publically accessible interface to receive response messages (confirm, failed, or event) from Provider NSA.

## Slide 8: What is a Requester-only NSA?
Is this the end user client?
Is this a delegate for end user requests (if so then is it not a Provider NSA from an end user perspective)?
Firewall
NSA A
NSA B
ReserveConfirm
Requester NSA
Firewall
ReserveRequest
Public IP address
Public IP address
Provider NSA
Clients
Clients
Clients

## Slide 9: Discussion
Is an NSA not an NSA?
  Requester and Provider are message exchange roles
  Having physically separate concepts has lead to additional confusion
What functionality can a Requester NSA support?
  Local NRM?
  Path finding?
  Aggregator?
  Service end-user client requests?
Do we administer Requester and Provider NSA differently?
  Should all NSA not be created equal, and therefore, meet the same deployment requirements?

## Slide 10: John’s Statements
NSA are fixed entities that actively participate in the NSI protocol.
Clients applications may be (and most often will be) transient entities that come onto and off of the network as needed by the application.
NSA are not transient entities since they maintain state of their associated connection reservations.
Client applications require a simple and lightweight connection services interface with different requirements and behaviors than an NSA.

## Slide 11: John’s Statements
The NSI-CS protocol as defined for NSA-to-NSA communications is complex, and will only get more complex as more features are added.
Application designers don’t like complex (they are a simple people).
Client applications will most likely be behind one or more firewalls will little ability to get special firewall configurations out of their IT department (application designers are crazy and cannot be trusted).

## Slide 12: Proposal
Leave NSI-CS transport protocol as is
  An NSA is an NSA so it must be publically accessible.
Provide a simplified client-specific representation of NSI-CS protocol interface
  A simplified subset of the existing NSI-CS capabilities.
  Firewall safe.
This interface should use current best practices for client API development
  RESTful definition.
  JSON/XML data representations.
  Useable from web-based clients.

## Slide 13: The RESTful Model
Firewall
End-user
Application
NSA A
Provider
Provider “NSA A” exposes publically accessible HTTP port.
“NSA A” maintains a “mailbox” for all events of interest associated with end-user reservation.
End-user issues requests using standard HTTP request/response model.
End-user does an HTTP long poll GET on a URL representing their mailbox.
“NSA A” places applicable event messages in response to this long poll (request can block for a short configurable period of time).
Firewall safe since End-user is creating out-bound socket request to a publically accessible port for both requests, and event retrieval.
Private IP address
Public IP address
POST Reservation
GET (ReservationState)

## Slide 14: Backup

## Slide 15: The Dedicated Socket
Firewall
NSA A
Requester
NSA B
Provider
Introduces a connection oriented transport protocol instead of the current “connectionless” model.
Provider “NSA A” exposes publically accessible TCP/IP port.
Requester-only “NSA B” opens a dedicate TCP connection to Provider “NSA A”.
All message exchanges between “NSA A” and “NSA B” occur through this dedicated socket.
Firewall safe since “NSA B” is creating an out-bound socket request to a publically accessible port, and there is no longer a need for replyTo field.
Private IP address
Public IP address
ReserveRequest
ReserveConfirmed

## Slide 16: The COMET Model
Firewall
NSA A
Requester
NSA B
Provider
Provider “NSA A” exposes publically accessible HTTP port.
Requester-only “NSA B” issues requests using standard HTTP request/response model.
“NSA B” requests URL for dedicated forwarding discriminator (FD) matching supplied filtering criteria.
“NSA B” does an HTTP long duration GET on the FD.
“NSA A” streams messages matching filter criteria (confirmed, failed, and event messages) over the FD HTTP socket.
Firewall safe since “NSA B” is creating out-bound socket request to a publically accessible port, and there is no longer a need for replyTo field.
Private IP address
Public IP address
ReserveRequest
ReserveConfirmed