## Slide 1: Future functionality of NSI
Tomohiro Kudoh (AIST)
NSI ad-hoc meeting
at GLIF2013 Singapore

## Slide 2
Transfer function description
Availability query
Support of non-network resources
Switching service
Protection
Smart aggregator
Federation
Cyclic/recursive use of NSA
Reactive behavior
Policy specification and enforcement
Monitoring

## Slide 3: 1. Transfer Function
“No-VLAN translation” is an example of the internal topology information
A, VLAN=80
A, VLAN=81
A, VLAN=82
A, VLAN=83
A, VLAN=84
B, VLAN=80
B, VLAN=81
B, VLAN=82
B, VLAN=83
B, VLAN=84
Jerry’s method

## Slide 4: Agreements at BTR meeting
An STP can have 0 or more <type,value> tuples =>
  STP (<network_id>, <local_id>, <type_1,value_1>, .. , <type_n,value_n>)
    e.g. STP (NetA, EndPt1, port, 1000, vlan, 123)
  Open question on how tuples can relate to one another, e.g. port 1-4 have vlans 1-4
  The STP specification incorporating the <type,value> tuples is stilljust a STP *identifier*. I.e. this in itself does not imply that these values are in any way related to specific technology or hardware features.
  On the other hand, <type,value> tuples can be used to define capabilities. The capabilities can describe technology, hardware, policy, or other limitations.
  The value of the "type" string is not defined as part of the NSI CS standard, i.e. it is defined as part of the service definition. The NSI CS standard only codifies the presence of <type,value> pairs as part of the STP identifiers. It is up to the provider (PA) to define them. However, we do expect that there will be a best-practices document describing some <type,value> combinations and capabilities.
The <value> filled can be an individual value or a range
  if a <value> is a range then it is a "STP_Bundle"
  i.e., these tuples may also be used to specify constraints that identify a set of STPs.
Open question on how we can describe constrains for STPs, e.g.
  STP (NetA, EndPt1, <port, $1>, <vlan, $2>)
  STP (NetA, EndPt1, <port, $3>, <vlan, $4>)
  Capabilities: $1 != $3, $2 = $4 => no vlan translation

## Slide 5: Procedural description of constraints
  If ($1 != $3 && $2 = $4)
  STP (NetA, EndPt1, <port, $1>, <vlan, $2>) and
  STP (NetA, EndPt1, <port, $3>, <vlan, $4>)
  cannot be interconnected.
Pros:
  Flexible
  Powerful
Cons:
  Needs additional syntax
  PF has to interpret the description to find constraints.

## Slide 6: 2. Availability query
In current protocol, RA cannot know resource availability without trying to make a reservation.
  If usage ratio is high, availability query will help finding available pathAvailability is just a “hint”.
  Each NSA can provide availability according to its policy.
    If not willing to provide such information, it is ok to provide no answer.
Existing advance reservation systems such as ones for airline/hotel reservation provide availability.

## Slide 7: What if?

## Slide 8: 3. Support of non-network resources
Computers, VMs, storages, humans…
By separating ServiceDefinition from main protocol, Current protocol can support reservation of anything
  Some name change is desirable
    ConnectionID -> ReservationID
    DataPlaneStatusChange -> ResourceStatusChange
    DataPlaneError -> ResourceError
  Is SD equivalent to Rspec (cf. GENI)?
NFV management

## Slide 9: 4. Switching Service
Takahiro Miyamoto-san
Can switching service be described by using ServiceDefinition?

## Slide 10: 5. Protection
Support of requesting/provisioning disjoint multiple paths between a pair of end-points
  MPTPC
  Protection
    1+n support is more complicated
Issues
  Request description (ServiceDefinition)
  Topology description and path finding
  Notification
    Huhnkuk Lim-san’s proposal and agreement made at Madrid OGF39

## Slide 11: 6. Smart aggregator
Chin Guok-san
Using NSI CS2.0, aggregator can do smart things which are not specified in the document
  Find alternative resource if a part of requested resources is not available
  Error handling, cf. NSA-based protection
May not require change of protocol itself, but such functionality of a NSA should be advertised.

## Slide 12: 7. Federation
NSI Federation model has not been defined yet
Layered(?) connection deployment
  Virtual connections belong to different tenants share a NSI provisioned connection
    Allow deploying multiple VLAN-connections or MPLS paths on a connection provisioned by NSI

## Slide 13: 8. Cyclic/recursive use of NSA
In current NSI CS protocol, a loop can be formed in service plane request paths
  An aggregator can hide its children (by its policy), and new connectionID will be created for child reservation.
  In NSI model, an aggregator can request to any other aggregator as long as trust relationship exists.
  No explicit way to prevent a looped request
    Moreover, recursive use of NSA is not always wrong.

## Slide 14: 9. Reactive behavior
Behavior based on data plane/user status
  Autonomous traffic engineering
    Increase bandwidth when load is high
  Data plane triggered reconfiguration
    Example: plugging in a device at any RJ45, connect the device to a certain slice (reservation) according to MAC address, etc. (OpenFlow)
Can STP be created dynamically?

## Slide 15: 10. Policy specification and enforcement
In NSI, each NSA can have its own policy
  But how to describe policy is not defined

## Slide 16: 11. Monitoring
Monitoring of dynamically provisioned infrastructure
  How to monitor “a slice”
  How to control access rights