## Slide 1: Building SDN with OGF NSI and OpenFlow
Takahiro Miyamoto
KDDI R&D Laboratories Inc.

## Slide 2: Software Defined Network
Software Defined Network (SDN) will be applied to various network.
Local-area (datacenter) network
Global-wide network
Most use cases target network operators who own physical network.
In my talk, I focus on virtual network over multiple networks.

## Slide 3: SDN over multiple networks

## Slide 4: SDN over multiple networks
How to create virtual (overlay) network topology?

## Slide 5: SDN over multiple networks
SDN over multiple networks should be built with two steps.
Create network skeleton.
  Node
  Link
Control network behavior.
Network skeleton
Software defined network
 OpenFlow
 OGF Network Service Interface
Node
Link

## Slide 6: OGF Network Service Interface (NSI)
NSI is designed to allow Grid, Cloud and other applications to mange network connectivity.
NSI also supports provider-to-provider circuit request.
NSI provides a framework for multiple services:
  Connection service
  Topology exchange service

## Slide 7: ConnectionService (NSI-CS)
Create point-to-point connections.
Support advanced reservation and immediate provisioning.
NSI-CS is promising service to create “Link” for network skeleton.

## Slide 8: SwitchingService (NSI-SS)
Be a new NSI service to realize multipoint network.
  Not a part of NSI yet.
Introduce a new endpoint called Switching Point (SP).
SP
SDP
STP
STP
create/delete SwitchingPoint
Connect between STPs
SwitchingService (SS)
ConnectionService (CS)

## Slide 9: OpenFlow switch on NSI-SS
SP is virtual OpenFlow switch.
SP
STP_a
SP is created via NSI-SS.
IP address of virtual OpenFlow switch is returned via NSI-SS.
OpenFlow controller connects to the virtual OpenFlow switch.
STP_b
STP_c
urn:ogf:network:example.com:2012:stp_a  port 1
urn:ogf:network:example.com:2012:stp_b  port 2
urn:ogf:network:example.com:2012:stp_c  port 3
OpenFlow controller
NSI-SS is promising service to create “Node” for network skeleton.

## Slide 10: Building SDN with OGF NSI and OpenFlow
1. Create network skeleton with NSI-CS and NSI-SS.
2. Control network behavior with OpenFlow.
Korea
Japan
US
EU
Hong Kong
OpenFlow controller

## Slide 11: Conclusion
SDN requires two network definitions.
  Network skeleton
  Transfer behavior  OpenFlow
OGF NSI is suitable to define network skeleton.
  ConnectionService = Link
  SwitchingService = Node
OGF NSI is essential technology in global-wide SDN era.