## Slide 1: OGF 25 2-6 March 2009 Catania, Italy NSI-WG Chain vs. Tree model
Radek Krzywania radek.krzywania@man.poznan.pl

## Slide 2: Chain model
Chain model assumes that nodes/domains are allowed to communicate only one-by-one, passing message from one to another

## Slide 3: Tree model
Tree communication model does not introduce „reachability” limitations, thus any node/domain can contact directly any other (despite if they are adjacent), also in simultaneous way

## Slide 4: Comparison – nodes order
Chain
Visited nodes has exactly defined order
Tree
There is no predefined order of reaching nodes

## Slide 5: Comparison – AAI
Chain
AAI consideration may base on neighbor trusts
Tree
AAI infrastructure needs to allow any-to-any communication

## Slide 6: Comparison – failure
Chain
Less flexibility in case of failure (chain break needed if intermediate node is down)
Tree
Flexibility in case of failure (can simply avoid not responding node)

## Slide 7: Comparison – request update
Chain
Next nodes along path may have access to previous nodes information (as request may be updated by them)
Tree
Nodes receives only request message; all information exchange between nodes needs to go through central point (request sender) or be independent messaging process between adjacent nodes

## Slide 8: Comparison – flooding and loops
Chain
Ordered messaging process allows to control messages loops and flooding
Tree
Flooding possible in one-to-many communication

## Slide 9: Comparison – Delivery time
Chain
Message delivery depends on number of hops between nodes
Tree
Immediate message delivery independent from nodes distance (hops) – at least theoretically

## Slide 10: Coexistence of methods
The coexistence of chain and tree communication model is supposed to be possible in some scenarios, however a detailed investigation is needed.
E.g. the chain and tree enabled nodes/domains should be grouped, otherwise tree enabled node may try to reach chain enabled nodes skipping the chain.

## Slide 11: Examples of messages processing Chain Model
Simple reservation request, where each object is expected to provide some resources

## Slide 12: Examples of messages processing Chain Model
Simple reservation request, where each object is expected to provide some resources
Objects are expected to respond one by one to the Object1 before sending request to next object
Messages forwarding mechanism

## Slide 13: Examples of messages processing Chain Model
Reservation request, which is forwarded through all objects, but responses are send individually to the Object1

## Slide 14: Examples of messages processing Tree Model
Request is sent to all objects (possibly at the same time) and each objects responds individually to the Object1. The order of responses is unpredictable.

## Slide 15: Chain and tree model in NSI WG
Both models can be used to achieve NSI goals, only the messaging process is different
NSI should not choose only one of the method, but should be opened to both (at the same time probably)
Messaging should not concern the real objectives of NSI, as this is mostly implementation issue, not architecture

## Slide 16: Thank you
Q&A, Discussions