## Slide 1: FELIX and NSI: Mutual Authentication and Authorization (Work in progress)
Presenter: Umar Toseef
OGF 43, Washington
26 March 2015

## Slide 2: Contents
FELIX background information
Authorization NSI
Proposed solution
Summary

## Slide 3
FELIX Background Information

## Slide 4: FELIX in a nutshell [1]
  EC (EU), MIC & NICT (JP) collaborative project
    Collaboration between European and Japanese partners
  Started in April 2013. To run till March 2016
PL
BE
NL
DE
IT
ES
JP
EU coordinator
JP coordinator
  To createa large-scale testbed (experimental infrastructure), federated across two continents
  To define a common software architecture for testbeds
Facts
Objectives

## Slide 5: FELIX in a nutshell [2]
OFELIA (OpenFlow in Europe: Linking Infrastructure and Applications)
  www.fp7-ofelia.eu
RISE (Research Infrastructure for large-Scale network Experiments)
  www.jgn.nict.go.jp/rise/english
Existing testbeds
To increase mutual benefits of European and Japanese researchers by creating more complex environments for specialized research and experiments
Why to federate?
Notes:   First large-scale OpenFlow-enabled experimental facility in Europe), continuously evolving through other FIRE projects (FIBRE, Fed4FIRE, ALIEN, etc.)
  OpenFlow testbed over JGN-X (the largest testbed network in Japan), with wide-area coverage from US West coast to Southeast Asia
  This opens up new opportunities for experiments due to geographical dispersion of testbeds
  By federating SDN islands, an integrated infrastructure can be constructed over globally distributed resources

## Slide 6: Inter-domain networking through NSI
RO: Resource Orchestrator, MRO: Master RO, VM: Virtual Machine, AM: Aggregate Manager,
RM: Resource Manager, SE-RM: Stitching Entity-RM, TN-RM: Transit Network-RM

## Slide 7: FELIX Clearinghouse
A trust anchor and responsible for authentication and authorization of all actors in a FELIX deployment
Supports extended Common Federation Service API version 2
Authentication using digital certificate
Certificate
  Asserts: public key ↔ subject
  Issued & digitally signed by clearinghouse CA
  Defined validity period
  X.509 version 3
Authorization using digital credentials
Credentials
  Provide the owner with permissions on a target object
  Issued & digitally signed by clearinghouse CA
  Defined validity period
  Can be delegated
  SFA and ABAC formats are supported

## Slide 8
Authorization in NSI

## Slide 9: Authorization in NSI
NSI is agnostic to authentication and authorization methods used by any network deployment
NSI introduces a flexible <sessionSecurityAttr> header element for transporting security related information between NSAs within the trusted control plane
The format of the any security related parameters inside the <sessionSecurityAttr> is left up to solution implementation
<sessionSecurityAttr> must be supplied by user/application to uRA for insertion in NSI request header
Security attributes are securely transported to all uPA involved in the reservation and consumed by their Authorization Server(s)
SURFnet deployment has employed OAuth token based authorization

## Slide 10: A depiction…
* Copied from John MacAuley’s presentation on NSI: Security Omnibus, Dec. 2014

## Slide 11: OAuth: Abstract protocol flow
Application
(client)
User
(Resource owner)
Authorization Server
Resource Server
1. Authorization Request
2. Authorization Grant
3. Authorization Grant
4. Access Token
5. Access Token
6. Requested resources
Authorization Server
User
(Resource owner)
0. User Registration
*Figure redrawn from RFC 6749

## Slide 12: Authorization in NSI using OAuth
Secure
Transport
uRA
AG
uPA
NRM
Authorization Server
1. Auth Grant
2. Access token
3. Access token + NSI
reservation request
4a. Access token
placed in NSI header
5. Extract access token
7. Confirm reservation
6. Validate access token
4b. Access token
placed in NSI header

## Slide 13
OAuth-based Solution for FELIX

## Slide 14: Trust between FELIX and NSI
Assumption: A central NSI Authorization Server exists per NSI deployment
Establish trust relationship between FELIX clearinghouse and NSI Authorization Server (analogous to user registration)
NSI Authorization Server adds FELIX clearinghouse’s root certificate in its Trusted Root Certificates
This way, NSI Authorization Server recognizes all certificates and credentials signed by FELIX clearinghouse
TN-RM obtains GENI styled digitally signed credentials by FELIX clearinghouse
TN-RM employs its credentials as ‘Authorization Grant’ to authenticate and authorize with NSI Authorization Server and obtain access token

## Slide 15: OAuth: Abstract protocol flow
FELIX
TN-RM
FELIX Clearinghouse
NSI
Authorization Server
NSI
AG/uPA
Digital credential
Digital credential
Access Token
Access Token
Requested resources
Trust

## Slide 16: FELIX and NSI: Authentication and Authorization
Secure
Transport
AG
uPA
NRM
NSI Authorization Server
1. Credential
2. Access token
3. Access token placed
in NSI request header
5. Extract access token
7. Confirm reservation
6. Validate access token
TN-RM
FELIX Clearinghouse
Credential
RO
MRO
4. Access token placed
in NSI request header
RO: Resource Orchestrator
MRO: Master RO
RM: Resource Manager
TN-RM: Transit Network-RM
Notes: TN-RM acts as uRA

## Slide 17: Important aspects of the proposed solution
Use of FELIX credential as ‘Authorization Grant’ complies with RFC 6749
NSI Authorization Server must NOT issue access token with validity period greater than that of TN-RM’s FELIX credential
In authorization process, NSI Authorization Server must validate presented credential and check whether privileges are sufficient to demand an access token
TN-RM’s FELIX credentials are issued and renewed by FELIX clearinghouse
TN-RM may use same access token for multiple resource requests
TN-RM may request access token more than once using the same credentials
The proposed approach could also be employed by other GENI/FIRE SDN testbeds

## Slide 18: Summary
FELIX project is about federation of SDN testbeds in EU and Japan
FELIX relies on NSI for multi-domain on-demand network connection services through transit network
OAuth can be used for NSI control-plane authentication and authorization
NSI Authorization Server establishes trust relationship with FELIX clearinghouse
TN-RM entity of FELIX acts as uRA when interfacing NSI world
FELIX clearinghouse issues GENI styled credential to its TN-RM entity
TN-RM exchanges its FELIX credentials to obtain access token
In future other methods for AuthN/AuthZ may also be supported

## Slide 19
Thanks for your attention
Acknowledgement:
Some figures and text are based on John MacAuley’s presentation on NSI: Security Omnibus, Dec. 2014