## Slide 1: Policy in GÉANT
Guy Roberts, Tangui Coulouarn
NSI meeting, NORDUnet Conference,
Uppsala, 22 Sept 2014

## Slide 2: AutoBAHN in GÉANT BoD
NSI v2.0 is used between all AutoBAHN instances
All AutoBAHN deployments in Europe operate identically (with the same code/modules) so that each instance can function as an RA, PA and simple Aggregator (AG).
Simple AG means that it follows the CHAIN model: It is capable of sending the request to its own PA and the next PA on the reservation path. (full AG facing other regions?)
AutoBAHN instances share NSI/NML topology via the AutoBAHN Topology Service. Centralized lookup service has an aggregated topology collected from local AutoBAHN instances.
Once topology exchange mechanism in NSI is standardized this will be adopted.

## Slide 3: AutoBAHN Path-finding
Inter-domain path-finding is normally performed at the start domain (source based routing).
AutoBAHN supports under-specified STPs in requests (port with a range of VLANs) to speed up reservation processing.
Can also support requests from RAs with specified VLANs.
AutoBAHN will honour ero’s in connection requests where possible.
AutoBAHN portal allows users to include/exclude certain segments from path.
Notes: Intra-domain
  Takes place at each domain
  Calculated on intra-domain (detailed) topology
  Provisioning technology specific information is considered
  Time variant information is considered (such as: resources utilization in a given time frame)

## Slide 4: Policies: AA at end-points
Transit traffic is accepted by default if a request comes from a trusted peering network (transitive trust).
For authentication purposes AutoBAHN tracks the origin of the request, this includes both user and source domain.
AA is performed at circuit end-points based on the policies of the local domain.
GÉANT needs a service that works now – complex transit policy can be added later.

## Slide 5: IP policy considerations in GÉANT
The GÉANT backbone does not allow transit of commodity IP.
Transit between two non-GÉANT NRENs requires special permission.
In general all other forms of transit are allowed in the backbone for GÉANT NRENs: NREN -> NREN and NREN -> commercial content providers.
IP policy is applied by an NREN adding the AS or IP prefix of an organization to their BGP configurations.
Institutions should only connect via their local NRENs.
Configuration of BGP simplified by the use of BGP peer groups
BGP is considered to be quite a coarse instrument for applying policy. Cannot be used to apply fine policy adjustment such as policy based on flow characteristics.
In no current need for similar policies in BoD service

## Slide 6
Thank you!