## Slide 1: A hierarchical, NSI compatible, topology proposal for NML
Jerry Sobieski
NORDUnet
Presented at OGF 34

## Slide 2: Hierarchical topology…
The existing NSI topology model does not provide a consistent mechanism for exposing intra-domain topological structure.
  The base model hides all internal structure…which is good in many (most) high level cases…. But…
  Where a network wishes to do so, it should be able to expose additional internal structure or state in a measured and graduated degree…down to the hardware minutia if so desired.

## Slide 3: NML recommendations
This proposal retains the NSI abstractions at the highest topological layer,
and retains the NSI model internally as smaller NSI domains are defined
A key relation called an “alias” is defined to link STPs (NML Ports) at any desired level to STPs at the next lower (more detailed) level.
  An Alias is an internal topological construct that should probably be stored at the lower level (more detailed level).
  It therefore stays private until/unless that level is announced externally. (local agents will not have a problem using this relation.)
An Alias could [alternatively] reference a conventional NML topological object – thus mapping the NSI topology to appropriate NML object as the local topology manager deems appropriate.

## Slide 4: NSI Topology Example Current existing NSI topology model: only L0 has structure, L1+ is opaque (private)
PSNC
Topo level 1
NetherLight
Topo level 1
Internet2
Topo level 1
NDN.EFDX
Opaque internal
Topo level 1
Universal space
Topo level 0
NetherLight-o
Internet2
Pionier
ION-o
NDN
NDN
NDN
SDPs (NML Links)
STPs (NML Ports)

## Slide 5: Proposed Hierarchical NSI Topology Example Proposed NorthernLight topology: L0 & internal L1 objects are publically announced by NorthernLight; As a Worldview, this topo would say I2, PSNC, and NL only announced L0 information. As a Local Topology from NDN, this is the only L0 information that NorthernLight can provide (i.e. its direct adjacencies)
PSNC
Topo level 1
NetherLight
Topo level 1
Internet2
Topo level 1
NDN.EFDX
Topo level 1
Universal space
Topo level 0
NYC Level 2
CPH
Level 2
NetherLight
Internet2
Pionier
NYC
AMS
POZ
NDN
CPH
ION
NDN
NDN
Blue links are “aliases” indicating an level transition in the topology. (Aliases act similarly to SDPs, so red and blue relations are simple logical links.)

## Slide 6: Hierarchical Topology Proposal Bi-directional Example
topo{ name $L0$; /* level 0 is the universal space */
topo{ name NDN.EFDX; version 2012-02-29-18:42:23 /* level 1 topology */
NSA https://orval.grid.aau.dk:9443/NSI/services/ConnectionService
port Pionier, NetherLight, Internet2 bidirectional;
topo{ name CPH; location lat 24.1234 lon -57.2345; /* level 2 topology */
port AMS, POZ, NYC bidirectional;
}
topo{ name NYC; location lat 24.1234 lon -87.2345; /* level 2 topology */
port ION, CPH bidirectional;
}
link NYC:CPH, CPH:NYC; /* level 2 to level 2 */
alias NDN.EFDX:Pionier, CPH:POZ; /* level 1 to level 2 boundary links */
alias NDN.EFDX:NetherLight, CPH:AMS; /* level 1 to level 2 boundary links */
alias NDN.EFDX:Internet2, NYC:ION; /* level 1 to level 2 boundary links */
}
Link NDN.EFDX:Pionier, Pionier.EFDX:NDN; /* NDN level 1 port to Pionier level 1 port */
Link NDN.EFDX:NetherLight, NetherLight.EFDX:NDN; /* level 1 port to level 1 port */
Link NDN.EFDX:Internet2, Internet2.EFDX:NDN; /* level 1 port to level 1 port */
}

## Slide 7: Uni-directional Circuits
Bi-directional and symmetric notions of “connections” are based in historical design of analog voice circuits where the same signal capacity was required in both directions
  This is clearly no longer the case with digital data telecommunications and networking.
Asymmetric flows (different BW requirements forward and reverse) have largely been ignored in conventional IP network engineering due to statistical multiplexing and assumption of balanced client-server distributions
  MPLS TE development has addressed issues of asymmetric loads
As applications begin to leverage NSI for performance guarantees, symmetric bi-directional connections will prove to be very inefficient use of transit resources and potentially limiting for
Uni-directional “connections” provide a more atomic service element for Connection Services such as NSI.

## Slide 8: NSI Topology Example Current existing NSI topology model: only L0 has structure, L1+ is opaque
PSNC
Topo level 1
NetherLight
Topo level 1
Internet2
Topo level 1
NDN.EFDX
Opaque internal
Topo level 1
Universal space
Topo level 0
Pionier-i
NetherLight-i
NetherLight-o
Internet2-i
Internet2-o
Pionier-o
ION-o
NDNi
NDNo
NDNi
NDNo
NDNi
NDNo
SDPs (NML Links)
STPs (NML Ports)

## Slide 9: Proposed Hierarchical NSI Topology Example Proposed NorthernLight topology: L0 & internal L1 objects are publically announced by NorthernLight; As a Worldview, this topo would say I2, PSNC, and NL only announced L0 information. As a Local Topology from NDN, this is the only L0 information that NorthernLight can provide (i.e. its direct adjacencies)
PSNC
Topo level 1
NetherLight
Topo level 1
Internet2
Topo level 1
NDN.EFDX
Topo level 1
Universal space
Topo level 0
NYC Level 2
CPH
Level 2
Pionier-i
NetherLight-i
NetherLight-o
Internet2-i
Internet2-o
Pionier-o
AMSi
POZi
NYCi
NYCo
AMSo
POZo
NDNi
NDNo
CPHo
CPHi
IONo
IONi
NDNi
NDNo
NDNi
NDNo
Blue links are “aliases” indicating an external level transition in the topology

## Slide 10: Hierarchical Uni-directional Topology Proposal Example
topo{ name $L0$; /* level 0 is the universal space */
topo{ name NDN.EFDX; version 2012-02-29-18:42:23 /* level 1 topology */
NSA https://orval.grid.aau.dk:9443/NSI/services/ConnectionService
port Pionier-i, NetherLight-i, Internet2-i inbound;
port Pionier-o, NetherLight-o, Internet2-o outbound;
topo{ name CPH; location lat 24.1234 lon -57.2345; /* level 2 topology */
port AMSi, POZi, NYCi inbound;
port AMSo, POZo, NYCo outbount;
}
topo{ name NYC; location lat 24.1234 lon -87.2345; /* level 2 topology */
port IONi, CPHi inbound;
port IONo, CPHo outbount;
}
link NYC:CPHi, CPH:NYCo; /* level 2 to level 2 */
link NYC:CPHo, CPH:NYCi; /* level 2 to level 2 */
alias NDN.EFDX:Pionier-i, CPH:POZi; /* level 1 to level 2 boundary links */
alias NDN.EFDX:Pionier-o, CPH:POZo; /* level 1 to level 2 boundary links */
alias NDN.EFDX:NetherLight-i, CPH:AMSi; /* level 1 to level 2 boundary links */
alias NDN.EFDX:NetherLight-o, CPH:AMSo; /* level 1 to level 2 boundary links */
alias NDN.EFDX:Internet2-i, NYC:IONi; /* level 1 to level 2 boundary links */
alias NDN.EFDX:Internet2-o, NYC:IONo; /* level 1 to level 2 boundary links */
}
Link NDN.EFDX:Pionier-i, Pionier.EFDX:NDNo; /* NDN level 1 port to Pionier level 1 port *
Link NDN.EFDX:Pionier-o, Pionier.EFDX:NDNi;
Link NDN.EFDX:NetherLight-i, NetherLight.EFDX:NDNo; /* level 1 port to level 1 port */
Link NDN.EFDX:NetherLight-o, NetherLight.EFDX:NDNi;
Link NDN.EFDX:Internet2-i, Internet2.EFDX:NDNo; /* level 1 port to level 1 port */
Link NDN.EFDX:Internet2-o, Internet2.EFDX:NDNi;
}

## Slide 11: Notes on NSI Uni-directional
Uni directional circuits do not conflict with existing bi-directional service
  Protocol remains the same.
  Some topology will need amending to reflect uni-directional STPs
  Reservation Req already has the directionality parameter – so this will make it useful
This will also cause the WG to think about “compositional” services
  E.g. How do you define a bi-directional connection pair that is either asymmetric or diverse
  How do we reference other Connections to specify things like parallel but reversed, diverse, etc

## Slide 12: Other Topological considerations
NML: Syntactic and name formalizations can be defined as make sense…just need to maintain NSI conceptual functionality.
  This is looking very good (Thanks to NML Freek, JdvH, Roman, Jason)
  We need to resolve some specification issues regarding topologies (e.g. do we nest them, or list them..) - not religious issues
NML: How do we map seemlessly from the abstract NSI constructs to the existing NML information?
  Again, I think this is syntactic mechanics…not a moral or theological issue

## Slide 13: Mapping NSI STPs to local detail
topo{ name $L0$; /* level 0 is the universal space */
topo{ name NDN.EFDX; version 2012-02-29-18:42:23 /* level 1 topology */
NSA https://orval.grid.aau.dk:9443/NSI/services/ConnectionService
port Pionier, NetherLight, Internet2 bidirectional;
topo{ name CPH; location lat 24.1234 lon -57.2345; /* level 2 topology */
port{ name=AMS; mode=bidirectional }
port{ name=POZ; mode=bidirectional }
port{ name=NYC; mode=bidirectional }
}
topo{ name NYC; location lat 24.1234 lon -87.2345; /* level 2 topology */
port{ name=ION; mode=bidirectional }
port{ name=CPH; mode=bidirectional }
}
link NYC:CPH, CPH:NYC; /* level 2 to level 2 */
alias NDN.EFDX:Pionier, CPH:POZ; /* level 1 to level 2 boundary links */
alias NDN.EFDX:NetherLight, CPH:AMS; /* level 1 to level 2 boundary links */
alias NDN.EFDX:Internet2, NYC:ION; /* level 1 to level 2 boundary links */
}
Link NDN.EFDX:Pionier, Pionier.EFDX:NDN; /* NDN level 1 port to Pionier level 1 port */
Link NDN.EFDX:NetherLight, NetherLight.EFDX:NDN; /* level 1 port to level 1 port */
Link NDN.EFDX:Internet2, Internet2.EFDX:NDN; /* level 1 port to level 1 port */
}

## Slide 14: Other Topological considerations
NSI: How does an NSA learn global topology…
NSI: How does an NSA announces or distribute their [public] topology…
NSI Decision point:
  Can we agree in principle to implement an “alias” [sdp] functionality in V2.0 ?
  Can we agree in principle to implement uni-directional Connections in V2.0 ? (details TBD)

## Slide 15: Merging topologies
Merging topologies- Intelligent semantic analysis of topology descriptions is necessary when merging two topologies:
  E.g. “link aruba:a1, bonaire:b1” is equivalent to “link bonaire:b1, aruba:a1”
  E.g. “port a1, a2, a3 inbound;” is equivalent to “port a1 inbound; port a3, a2 inbound;”
  E.g. “topo{ link a,b; topo{…}; }” is equivalent to “topo{ topo{…}; link a, b;}”

## Slide 16: Topology issues addressed BTR
Type Value pairs
  The issue was how to express “other information” associated with STPs
  Proposed: field separators are tbd
    <STP> := <network> “:” <locid> [“,” <TVP> ]*
    <TVP> := <type> “=“ <string>
    Example: esnet.ets:ps80,vlan=1780
  STPs are *still* identifiers – how the TVP types and associated values are used is a service specific
  Thus, a Reservation Req could submit:
      Source= “nl:cph1,port=ge0/1/4,vlan=4000”
      Dest= “ndn:cph2-xe3/2/1.2001”

## Slide 17: Mapping NSI STPs to local detail
NSI Network{ name NDN.EFDX; version 2012-02-29-18:42:23
NSA https://orval.grid.aau.dk:9443/NSI/services/ConnectionService
STP{ name=“NDN.EFDX:Pionier,vlan=4000” bidirectional }
STP{ name=“NDN.EFDX:NetherLight,vlan=4001” bidirectional }
STP{ name=“NDN.EFDX:Internet2,vlan=4002” bidirectional }
SDP “NDN.EFDX:Pionier,vlan=4000”, Pionier:CPH1;
SDP “NDN.EFDX:NetherLight,vlan=4001”, Netherlight.EFDX:CPH4001;
SDP “NDN.EFDX:Internet2,vlan=4002”, ION.EFDX:NDN-NYC;
}

## Slide 18: Mapping NSI STPs to local detail
topo{ name $L0$; /* level 0 is the universal space */
topo{ name NDN.EFDX; version 2012-02-29-18:42:23 /* level 1 topology */
NSA https://orval.grid.aau.dk:9443/NSI/services/ConnectionService
port Pionier, NetherLight, Internet2 bidirectional;
topo{ name CPH; location lat 24.1234 lon -57.2345; /* level 2 topology */
port{ name=AMS, mode=bidirectional,
mapsTo=“router=cph-nsi.nordu.net, port=ge0/0/10, unit=1780”;
port{ name=POZ, mode=bidirectional,
mapsTo=“router=cph-nsi.nordu.net, port=ge0/2/0, unit=1780”;
port{ name=NYC, mode=bidirectional,
mapsTo=“cph2-nsi.nordu.net eth0.1780”;
}
topo{ name NYC; location lat 24.1234 lon -87.2345; /* level 2 topology */
port{ name=ION, mode=bidirectional,
mapsTo=“router=nyc-nsi.nordu.net, port=ge2/19, unit=1780”;
port{ name=CPH, mode=bidirectional,
mapsTo=“router=nyc-nsi.nordu.net, port=ge2/12, unit=1780”;
}
link NYC:CPH, CPH:NYC; /* level 2 to level 2 */
alias NDN.EFDX:Pionier, CPH:POZ; /* level 1 to level 2 boundary links */
alias NDN.EFDX:NetherLight, CPH:AMS; /* level 1 to level 2 boundary links */
alias NDN.EFDX:Internet2, NYC:ION; /* level 1 to level 2 boundary links */
}
Link NDN.EFDX:Pionier, Pionier.EFDX:NDN; /* NDN level 1 port to Pionier level 1 port */
Link NDN.EFDX:NetherLight, NetherLight.EFDX:NDN; /* level 1 port to level 1 port */
Link NDN.EFDX:Internet2, Internet2.EFDX:NDN; /* level 1 port to level 1 port */
}

## Slide 19: Other Related STP/SDP issues TBD
Enumeration:
  How do we define large sets of similar STPs?
  <network><locid> [ , <TVP>]*
  <TVP> := <type> “=“ <value> [“..” <value>]*
Path Guidance (anypoint guidance)
  Source/Dest set specification
    Ex: destination= esnet:ps[0..100,102,104,177] any *one* of these STPs is acceptable
  Loosen the endpoint constraints
    Ex: destination= esnet:* (any available STP in esnet)
      esnet:*! (first available STP inside esnet)
      esnet:~ (transit esnet )
  Some of these require an “ero” style capability
  These are critical to solving exhaustive search issues