## Slide 1: NSI in the SDN Environment (from perspective of an NSI fellow)
Jerry Sobieski
NORDUnet
Presented to
OGF 36
Chicago, US
October 8, 2012

## Slide 2: What is “SDN”?
SDN:= “Software Defined Networking”
  Networks defined according to the needs of software/applications using them
  Networks that are configured/reconfigured via software tools
  Networks where the control plane and data plane are separated
N1
L1
X
CP
N2
X
CP
C1
N1
L1
X
CP
X
M2
N2
M1
M2
M1
Conventional switching architecture
M1 & M2 are proprietary,
Ctrl Plane dominated by standardized distributed protocols
Ctrl plane
Data plane
SDN switching architecture
M1 & M2 are open and standarized, e.g. OpenFlow,
Ctrl Plane collapsed to a central “user” software agent

## Slide 3: Networks
Networks are distributed systems designed to move data from one location to another
Networks are [still (!)] characterized as graphs comprised of several key elements:
  Nodes – where switching or forwarding rules are applied to move traffic through the network
  Links – transparent conduits that carry information between nodes
  Ports – differentiate/identify links that converge on a single node.
N1
N2
N3
L3
L2
L1
P0
P1
P2
P3
P4
P5
N1
N2
N3
P0
P0
P4
P5
L1
L3
L2
P1
P0
P1
P1
P1
P0
P1
P0
Conventional Graph
Resource Graph
A
Z
A
Z
LZ
LA
P2
P3

## Slide 4: Architectures to Infrastructure
Architecture
Infrastructure
CHI
AMS
Control
Push
Forwarding/Switching
Fabric
Push
Push
Push
Pop
Pop
Pop
Pop
X
X
X
X
X
X
X
X
X
X
X
X
X
CPH
WDC
TOK
X
X
X
X
Real World global production transport infrastructure

## Slide 5: NSI features relevant to SDN
NSI is an inter-domain framework
  It is a self consistent, distributed, peering model
  It abstracts transport services – extremely versatile.
  It defers intra-domain specifics to the “network resource manager” (NRM)
  Security is designed in…NSI Defines clear inter-domain service boundaries and insures that all interactions across those boundaries are authorized.
NSI-CS is explicitly designed to provide simple transparent conduits for the delivery of data from one location to another.
From a NSI perspective:
  the NRM function maps well to an SDN Controller agent or hypervisor managing internal switching and forwarding configurations…
From an SDN perspective,
  the SDN controller/hypervisor agent can utilize NSI protocol(s) to acquire and manage transport resources beyond (or underlying) its local service domain
  i.e. the Hypervisor can easily be an NSA for its domain

## Slide 6: NSI features relevant to SDN
NSI is technology agnostic
  It does not dictate specific intra-domain technologies
  Thus novel switching technologies such as OpenFlow are easily accommodated.
NSI is a framework that neatly integrates several key atomic functions of modern networks that map to SDN:
  SDN is about switching and forwarding – atomic “Nodes” - these map very nicely to NSI network service domains.
  NSI is about transport services – atomic “Links” - that carry data between/across intermediate devices/domains, whatever those domains may contain…
NSI already recognizes the separation of control and data plane:
  It has the NSA control plane agents and the NSI Network objects that comprises the data transport plane.
  It asserts neither an in-band nor a congruent control network NSAs simply speak for their domain
  NSI does not differentiate users from network – any user is able to take advantage of the full features of NSI framework

## Slide 7: NSI as basic transit provider
The inter-domain transport model:
  NSI-CS is used to establish transparent conduits between SDN domains.
  These Connections create SDN adjacencies over/thru intervening multi-layer transit networks
    The NSI domains are opaque - they just provide the basic atomic network function of transparent transport links.
  This model recognizes real world MAN/WAN transport engineering issues
X
CP
X
X1
CP
X2
NSA
NSA
NSI Enabled
SDN Controller
Intervening opaque
NSI transport domains
NSI
NSI
NSI
No change internally
to the SDN architecture or operation
The SDN environments are topologically adjacent by merit of
NSI established transparent connections

## Slide 8: SDN transit facilities under NSI
The SDN based transit network service model:
  NSI-CS is used to provision connection requests across an SDN environment.
  This model allows NSI-CS to offer SDN flow spaces via the n-tuple STP mapping.
    Enables “flow space defined” transport links connections.
    It is consistent with NSI abstractions (domain boundaries, STPs, etc.)
X
CP
X
X1
CP
X2
NSA
NSA
NSI peer network
Transit networks using SDN
Technologies internally
NSI
NSI
NRM
NSI is used as the east/west interface across SDN domains to establish end-to-end connectivity
NSA
Integrated
NRM
X1
X2
X3
X1
X2
X3
NSI peer network
NSI
NSI transit networks

## Slide 9: SDN Slicing using NSI
The SDN agents construct slices using the NSI provisioning to link slivers in diverse locales
  Provides ultimate control to SDN users to dynamically construct slices globally with application specific topologies.
Y
Ctlr
Y
Y
X
X
Ctlr
NSA
Federating
NSA
NSI
BlueY links
Independent SDN
enabled facilities
NSI
GreenX links
NSI provisioned
metro/regional/longhaul
transport networks
NSA
NSA
KISTI
Univ. of
Houston
Frederica
GreenX Slice
BlueY Slice

## Slide 10: NSI STPs and Flow Spaces
NSI STPs currently include virtual constraints such as stacked VLANs, MPLS labels, timeslots, etc.
NSI STPs can as easily include physical interface lists, TCP ports, IP addresses, mac addresses, protocol IDs, or even ranges of these characteristics
NSI Service Termination Points (STPs) are described by an “n-tuple” that contains a set of topological elements in the form of type-value pairs that uniquely identify differentiate the traffic belonging to a particular connection from all other traffic crossing the domain boundary.
  STP aruba:a := <topo=NORDUnet>, <metro=CPH>,<sw=mx80a>, <slot=0>, <if=3>, <port=0>, <orientation=inbound>, <vlan=100>, <innertag=4>
  STP nordunet:umd-client :=<sw=CPH>, <slot=0>, <pic=2>, <port=0..3>, <vlan=2001..2099>, <srcmac=03ae0c******>, <sourceIPaddr=128.8.120/24>
An STP is a set of constraints that identify a flow (!)
NSI Connections – in the context of NSI network service domains- can be modeled as an SDN action rule:
  If packet=<ingress STP tuple> then action=[forward <egress STP tuple>]

## Slide 11: NSI STPs and Flow Spaces
Issue that need to work out:
  NSI v2 Resv() request does not currently recognize a flow space.
    It allows for T-V pairs that identify a group of termination points as source or destination.
    Such a specification could also define a flow space
  What happens if STP flow spaces intersect?
    In SDN, flow spaces are prioritized so that packets fall thru the sieve in certain orders… Does SDN/OF support multi-matching of flow rules?
    In NSI, what happens if an STP A:= <..>,<vlan=1..100> is defined and another STP B:=<…>,<vlan=51..150>
    a) how are these specs interpreted? as 100 separate STPs? Why? Why not a flow space of traffic from any of those 100 VLANs?
  How do SDN practitioners perceive of “domains”?
    Is this a techno-theoretical model? Or does this allow for the real world aspects of security and privacy and policy dictated by funding bodies and legal requirements?

## Slide 12: Inter-Domain NSI Flow Spaces?
The question has been posed:
How can we distribute “Flow Spaces” to different domains/networks?
Could NSI be instrumental for doing this?
Why would anyone want/need to distribute flow spaces?
  A flow space by itself is simply a set of constraints that define a set of packets…it does not implicitly specify an action to be performed on those packets (!)
  For a flow spec to be useful, it must be part of a “rule” – some explicit or implicit action(s) to be performed when the packet(s) are matched.
So… Can NSI framework be used to express “rules” across domain boundaries?
  If we define a rule to contain a sourceSTP (the source flow space), and an action to be performed to reach the terminal state i.e. the “destinationSTP” (the egres, then a rule does represent a flow, or connection, with both ingress specification and egress specification.
  This is admittedly not a conventional notion of a switching domain – but that seems altogether consistent with SDN clean slate out-of-the-box aspirations…

## Slide 13: Final Thoughts
We are in a world of virtualized multi-layer multi-domain networks and applications
  There *will* be layers above and below that we will not perceive or have access to.
  And there will be networks or domains that we will need to interact/interoperate with – that are not homogeneous
It seems futile to presume there will ever be just one layer or technology
  We must not promulgate technologies or protocols that cannot exist in such multi-layer, multi-domain environments…
How do we interoperate across/with domains where we cannot dictate how networks or applications must be constructed or operated?
  Is it possible to define an abstract interchangeable multi-layer model that can used generally ?
  Are there atomic principles and functions we can agree on that apply to all layers/regions of modern

## Slide 14: Summary
NSI is a framework for inter-domain exchange of information to effect several important global services:
  Inter-domain transport link provisioning, Scalable topology distribution
  Others tbd: Performance Verification, …
SDN is a model for defining the intra-domain forwarding and switching behaviour of networks
  It provides for user control, It standardizes the interface to the forwarding elements
  It provides a much richer set of forwarding capabilities than conventional hardware.
SDN needs NSI to provide a means for interoperating with and transiting the space between/under/across “SDN” domains to construct the rich topology that SDN networks expect.
NSI and SDN are complementary aspects of fundamental network architecture.
The NSI WG should explore how SDN principles (broadly construed) can be more thoroughly integrated into the NSI inter-domain framework.
X1
CP
X2
X2
X1
CP
X2
X2
X1
CP
X2
X2
NSI
OpenFlow
OpenFlow
OpenFlow
NSI
NSI
NSI

## Slide 15
The End