## Slide 1: GEANT OpenCall – NSI CONTEST
NSI CONTEST – Demonstrator
Giacomo Bernini
Nextworks
OGF43 @ GENI Networking Conference 22,
25-27 March 2015, Washington DC

## Slide 2: Summary
NSI CONTEST project
Testing NSI implementations using NSI CONTEST
NSI CONTEST Demonstrator

## Slide 3: NSI CONTEST project

## Slide 4: NSI-CONTEST: Main Objectives
Provide a new framework for validating the compliance of BoD systems with the NSI Connection Service v2.0 protocol
Design and develop a set of tools constituting the NSI CS v2.0 Conformance Testing Suite
Produce complete documentation of test scenarios and usage guides for software developers to run specific tests against the suite
Provide online platform for testing

## Slide 5: What can be tested
Message testing
    syntax and semantics checking for parameters
    recording message flows
Workflows testing
  Custom test cases
    includes also predefined test cases with typical scenarios for requester, provider and aggregator agents
  State machines validation
  Simulating different behaviours and conditions:
    unexpected situations (i.e. going down) and generating different error events
    timeouts
    NRM processing time

## Slide 6: CTS Architecture Testing Workflows

## Slide 7: NSI v2.0 CTS High Level Architecture
Mock NRM
NSI-RI
Local Test Runner
Mock NRM
NSI-RI
Local Test Runner
Mock NRM
NSI-RI
Local Test Runner
NSI CTS
Web Portal
NSI developer implementation
NSI v2.0 messages
Test coordinator
Rabbit MQ
Local Test Descriptors
Local Test Results
Test spec
Test result

## Slide 8: Workflow description – running tests
Step 1: Register to the NSI CTS web portal
Step 2: Select one of the predefined template for the test
Step 3: Configure and prepare the test for running
Configure NSI suite under test
Configure the test template parameters
Step 4: Start the test scenarios from the NSI CTS web portal
All the NSI RI instances and test procedures are automatically started from the NSI CTS
Step 5: Results collected and stored in the NSI CTS portal
NSI developer’s actions to validate an NSI CS v2.0 protocol stack

## Slide 9: NSI-CTS web portal
Project corresponds to a single User NSI Instance:
define configuration details
provide common topology for all scenarios
test cases are based on the predefined template scenarios
Test Case is a set of tests to validate the compliance of the User NSI Instance with the NSI CS v2.0 protocol.
Template – predefined reusable definition of a single test scenario
Test specification
Test
results

## Slide 10: Test Scenario
A single test executes all the actions defined in a template scenario
The test result highlights proper and invalid situations related to User’s SUT

## Slide 11: Demonstrator

## Slide 12: The NSI-CONTEST demonstrator in a glance
Pre-configured templates to validate the main NSI CS v2.0 protocol procedures for reservation, provisioning, release and terminate actions
  Direct check of NSI messages from NSI client instance and indirect verification of NSI FSMs
  Emulation of successful and failed scenarios
Test of requester and provider agents
  Provider test: the NSI-RI acts as requester agent and generates the NSI messages specified in the test description
  Requester test: the NSI-RI acts as provider and validates the NSI messages received from the SUT
    Comparison with the expected NSI messages specified in the test description

## Slide 13: Test runner and test descriptors
Mock NRM
NSI-RI
Local Test Runner
Test results
NSI
operations
config
NSI developer implementation
NSI v2.0 messages
REST APIs
POST (test spec)
GET (test result)
Test spec in the NSI CTS web portal
Configuration (ports, endpoints, NSA names)
Test workflow
  NSI message generation
  Expected messages from NSI peers
  Expected message contents
  Behaviour on failures
  Time intervals and timeouts
NSI CTS

## Slide 14: Test descriptor example: SUT as provider
<scenario id="1" peer="ciccio">
<description>TESTCASE_NAME</description>
<configuration>
<option name="nsi_listen_port" value="9090" />
<option name="reply_to_endpoint" value="http://127.0.0.1:9090/nsicontest/ConnectionRequester" />
<option name="remote_endpoint" value="http://127.0.0.1:9091/nsicontest/ConnectionProvider" />
<option name="provider_nsa" value="test.provider" />
<option name="requester_nsa" value="test.requester" />
</configuration>
<section id="sect1" interval="500">
<operation id="oper1" name="reserve" interval="2500" continueOnError="false" expected="reserveConfirmed" />
<operation id="oper2" name="reserveCommit" interval="2500" expected="reserveCommitConfirmed" />
<operation id="oper2" name="provision" interval="2500" expected="provisionConfirmed" />
<operation id="oper2" name="release" interval="2500" expected="releaseConfirmed" />
<operation id="oper2" name="terminate" interval="2500" expected="terminateConfirmed" />
</section>
</scenario>

## Slide 15: Test result example: SUT as provider
<section id="sect1" interval="500">
<operation interval="2500" continueOnError="false" failOperation="false" expected="reserveConfirmed" name="reserve" id="oper1">
<result>
<success>true</success>
<receivedEvent>response.reserveConfirmed</receivedEvent>
</result>
</operation>
<operation interval="2500" continueOnError="false" failOperation="false" expected="reserveCommitConfirmed" name="reserveCommit" id="oper2">
<result>
<success>true</success>
<receivedEvent>response.reserveCommitConfirmed</receivedEvent>
</result>
</operation>
[…]
</section>
<section id="sect1" interval="500">
[…]
<operation interval="2500" continueOnError="false" failOperation="false" expected="releaseConfirmed" name="release" id="oper4">
<result>
<success>false</success>
<receivedEvent>response.releaseFailed</receivedEvent>
</result>
</operation>
[…]
</section>
Successful result
Failed result

## Slide 16: Test descriptor example: SUT as requester
<scenario id="1" peer="ciccio">
<description>TESTCASE_NAME</description>
<configuration>
<option name="nsi_listen_port" value="9090" />
<option name="reply_to_endpoint" value="http://127.0.0.1:9090/nsicontest/ConnectionRequester" />
<option name="remote_endpoint" value="http://127.0.0.1:9091/nsicontest/ConnectionProvider" />
<option name="provider_nsa" value="test.provider" />
<option name="requester_nsa" value="test.requester" />
</configuration>
<section id="sect1" interval="500">
<operation id="oper1" name="listen" expected="reserve“ failOperation=“false”>
<!-- expectedRequestedNSA="sut.requester.nsi.1"
<match name="startTime">2014-06-21 15:50:10.000 GMT</match>
<match name="startTimeMin">2014-06-21 15:50:10.000 GMT</match>
<match name="startTimeMax">2014-06-21 15:50:10.000 GMT</match>
<match name="endTime">2014-06-21 15:55:10.000 GMT</match> […]
<match name="version">0</match>
<match name="versionMin">0</match> […]
<match name="bidirectional">true</match>
<match name="symmetricPath">true</match>
<match name="capacity">9600</match> […]
<match name="requestedDestStp">urn:ogf:network:test.provider:2013:topology:egress?vlan=1000-2000</match> […]
-->
</operation>
<operation id="oper1" name="listen" expected="reserveCommit" />
<operation id="oper1" name="listen" expected="provision" />
<operation id="oper1" name="listen" expected="release" />
<operation id="oper1" name="listen" expected="terminate" />
</section>
</scenario>

## Slide 17: Demo scenarios
Demo 1: SUT as provider
  Verify NSI message exchange for successful or failed reservation and provisioning actions triggered by the NSI-RI instance
Demo 2: SUT as requester
  LISTEN operations and successful responses @ NSI-RI instance
  Validation of format and contents of RESERVE, RESERVE-COMMIT, PROVISION, RELEASE and TERMINATE messages

## Slide 18: Thank you!
Giacomo Bernini
g.bernini@nextworks.it
Nextworks s.r.l.
Via Livornese 1027, 56122 Pisa (IT)
(+39) 050 3871 696