## Slide 1: OGF NSI CS Protocol State Machine
Converged single view
July 16, 2011

## Slide 2
NSA
NSA
NSA
NSA
NRM
NRM
NSI messages
Input/output internal events
RA
PA
RA RA
PA
RA
PA
Originator
Aggregator
Ultimate Provider
Aggregator/
Ultimate Provider
NRM
State machine
Timer
Network Resource Manager

## Slide 3: NSA State Machine
A generic state machine which incorporates all of the possible operational modes: originator, aggregation and ultimate provider.
Inputs/Outputs are:
  NSI messages
  NSA internal events
A Mealy machine
  Outputs are associated with transition edges
Input Event
Input Message
Output Message
Output Event
Inputs which trigger a state transition
Outputs associated with the transition

## Slide 4: Primitives: NSI messages
Primitive | Description
reservationRequest (Confirm/Failed) rsv.rq, rsv.cf, rsv.fl | the RA requests the PA for reservation of network resources for a connection between two STP’s constrained by certain service parameters
provisionRequest (Confirm/Failed) prov.rq, prov.cf, prov.fl | the RA requests the PA to provision a reservation (associated with a previous reservation message)
releaseProvisionRequest (Confirm/Failed) rel.rq, rel.cf, rel.fl | the RA request for the PA to de-provision resources without removing the reservation
terminateReservationRequest (Confirm/Failed) term.rq, term.cf, term.fl | the RA request for the PA to release the provisioned resources and terminate the reservation
forcedEndRequest fcd_end | This is reported by the PA to the RA to notify that the PA has forced an termination of the reservation
queryRequest (no side effects, not in the state machine) | mechanism for either RA or PA to query the other NSA for a set of connection service instances between the RA-PA pair. This message can be used as a status polling mechanism

## Slide 5: NSA internal events
SM -> NRM
  reservation: reserve the requested resources on the local NRM.
  provision: provisioning of resources within local NRM
  release: release of resources within the local NRM
  terminate: terminate of a reservation within local NRM
NRM -> SM (reply)
  *_cf: the requested action in the local NRM was completed successfully..
  *_fl: the requested action failed in local NRM.
NRM -> SM (asynchronous event)
  forced_end: resources allocated to the schedule were (administratively) released by the local NRM
Timer -> SM
  start_time: start time of the reservation has been reached
  end_time: end time of the reservation has been reached

## Slide 6: States
State | Description
Initial | nothing exist yet, the RA and PA are waiting the user initiation
Reserving | a reservationRequest has been sent and the PA is attempting to make a reservation
Reserved | the reservationRequest has succeeded and a reservation has been created. Note that here the provisioning state is either unprovisioned or indeterminate
AutoProvision | A reservation is present and a provisionRequest has been received, waiting for the startTime to arrive so that automatic provisioning can be initiated
Scheduled | the reservation is active (after the startTime), however either a provisionRequest has not been received yet, or the provisioning has been released
Provisioning | both a provisionRequest has been sent and startTime has arrived, so provisioning is ongoing
Provisioned | the Connection has been correctly provisioned
Releasing | a releaseRequest has been sent and a release is ongoing
Cleaning | a reservationFailed message has been received so the reservation is being cleared
Terminating | a terminateRequest message has been sent and the reservation and if necessary the provisioning are being removed
Terminated | nothing exists any longer, a terminate request has been successful

## Slide 7: State Machine Notation
Message direction
  > :Downstream input/output
  < :Upstream input/output
Combined input events
Inputs are not consumed until processed
  Unprocessed inputs are preserved after transitions
When all possible messages and event are received
When one or more message or event is received
When messages/event is received from all possible children, and one or more of them is .fl or _fl
When .cf or .fl messages and _cf or _fl events are received from all the children

## Slide 8: Combined State Diagram with events and NSI messages
Reserving
Scheduled
Provisioned
Provisioning
Releasing
Initial
Terminated
Any
State*
Terminating
Cleaning
Reserved
Auto
Provision
>rsv.rq
>rsv.rq
(reservation)
(reservation_cf)
<rsv.cf
<rsv.cf
(reservation_fl)
<rsv.fl
<rsv.fl, >term.rq
(terminate)
>term.rq
>term.rq
(release)(terminate)
>prov.rq
>prov.rq
(start_time)
(start_time)
(provision)
>prov.rq
>prov.rq
(provision)
(provision_cf)
<prov.cf
<prov.cf
(provision_fl)
<prov.fl
<prov.fl
>rel.rq
>rel.rq
(release)
(release_cf)
<rel.cf
<rel.cf
(release_fl)
<rel.fl
<rel.fl
(forced_end)
<fcd_end
<fcd_end, >term.rq
(release) (terminate)
(terminate_cf)
<term.cf
(terminate_cf)
<term.cf
<term.cf
>prov.rq
<prov.fl
>rel.rq
<rel.fl
>term.rq
<term.fl
(provision_cf)
<prov.cf
<prov.cf
(release_cf)
<rel.cf
<rel.cf
(terminate_cf)
<term.cf
<term.cf
(reservation_fl)
<prov.fl
<prov.fl
(release_fl)
<rel.fl
<rel.fl
(end_time)
(release) (terminate)
(reservation_fl)
<rsv.fl
<rsv.fl
(reservation_cf)
<rsv.cf
<rsv.cf
>prov.rq
<prov.cf
*: excluding “Initial”, “Cleaning”, “ Terminating” and “Terminated” states
>rel.rq
>rel.rq
(release)
(terminate_fl)
<term.fl
<term.fl

## Slide 9: Appendix: Manual and Auto provisioning
rsv.rq
rsv.cf
prov.rq
Prov.cf
rel.rq
rel.cf
prov.rq
Prov.cf
term.rq
term.cf
Start time
Requester
Provider
In service
In service
Reserved
rsv.rq
rsv.cf
prov.rq
prov.cf
rel.rq
rel.cf
prov.rq
Prov.cf
term.rq
term.cf
Start time
Requester
Provider
In service
In service
Reserved
Manual Provisioning
Automatic Provisioning