## Slide 1: NTT’s SC11 Demo Plan
2011.7.16
Akeo Masuda
NTT Labs.

## Slide 2: QoS-aware path selection for multi-domain datapaths
Legacy services only needed shortest-path calculation
  PSTN: QoS was assumed to be guaranteed in every domain
  Internet: You can’t expect QoS, it’s “best effort”
QoS is one of the future concern in the wide-area wide-band connection service
  Long-distance path consisted of circuits offered by domains with various technology
  Wide range of requirements by future applications
Performance measurements are necessary to select the best path
  For QoS factors that are fixed (E2E delay, MTU, Capacity, …)
  For QoS factors that fluctuate by cross-traffic effects (jitter, packet loss, …)
    “Bandwidth reservation” does not always mean QoS is guaranteed
    You also need to monitor the performance even after you start using the path

## Slide 3: Architecture
Request for measurement results
Request for triggering measurement event
ex) perfSONAR protocol
Resource allocation
Path setup request
ex) PN Manager API (NTT)
QoS –aware PCE
Circuit reservation request
(by chain or tree signaling)
ex) OGF NSI
    User interface
    Path calculation and selection
    Admission control and management of requested circuits
    Optimization of virtual network topology (VNT)
Network Controller
Reservation Agent
VNT Manager
  Path setup control
    Virtualization of network resources
Measurement point
Measurement Archive
Monitoring Manger
Resource manager
The QoS-aware PCE receives the path request with performance requirements from the user
It selects the best path, and requests the circuit to each of the domains
Reservation Agent
Physical Network Manager
Monitoring Platform
User client
    Path request with QoS requirements
    ex) PCEP, NSI, Web UI

## Slide 4: SC10 demo: Network Virtualization
LA
Seattle
SLC
KC
Houston
Chicago
NY
DC
Atlanta
SC10 booth #1521
New Orleans
Osaka
Traffic Generator
Video Server
Routers
1G
10G
OXCs
DCN nodes
DCN domains
GMPLS Domain
Tokyo
Tokyo
1 to n network virtualization to conduct 3 experiments upon JGN2plus
n to 1 network virtualization to construct a wide-area virtual network formed by multi-domain paths
PN Manager
VN Agent
VN#1: Dynamic VNT reconfiguration
VN#2: Uncompressed HDTV transmission
VN#3 Wide-area virtual network using multi-domain/multi-technology paths
測定装置
映像伝送装置
DCN path

## Slide 5: SC10 demo: Topology visualization
perfSONAR TS
VN Agent
<nmtopo:topology xmlns:nmtopo= "http://ogf.org/schema/network/ topology/base/20070828/">
<ns1:domain xmlns:ns1="http://ogf.org/schema/network/topology/ ctrlPlane/20080828/" id="urn:ogf:network:domain=xxx.internet2.edu">
<ns1:node id="urn:ogf:network:domain=ion.internet2.edu:node= rtr.xxx">
<ns1:address>xx.yy.zzz.xx</ns1:address>
<ns1:port id="urn:ogf:network:domain=xxx.internet2.edu: node= rtr.xxx:port=xe-1/0/0">
<ns1:capacity>10000000000</ns1:capacity> <ns1:minimumReservableCapacity>1000000</ns1:minimumReservableCapacity>
<ns1:granularity>1000000</ns1:granularity>
<ns1:link id="urn:ogf:network:domain=xxx.internet2.edu: node=rtr.xxx:port=xe-1/0/0:link=xe-1/0/0.0“>
:
GUI
Internet2 ION
SCinet
JGN2plus
GMPLS network

## Slide 6: SC10 demo: Reservation request GUI
Select/drag endpoint nodes
pop-up window appears
Select path configuration details (pull down)

## Slide 7: SC11 Demo plan
We enhance the DCN client GUI to support NSI requester agent
Provision global paths (trans-Atlantic and trans-Pacific) and measure the performance
Demonstration/Experiments:
  Graphical simulation of measurement-based path selection
  Application-driven global path switchover without packet loss
    (Switches over to better path, according to the performance fluctuation)
US
Asia
Atlantic Ocean
Pacific Ocean
Europe
Internet2
SCinet
JGN-X
GEANT2 BoD or static
NTT Labs
MANLAN
TEIN3 (L3)
GEMNET
JANET
IP-optical NW
Dynamic Path
Static path
DCN/AutoBAHN or NSI
DCN or NSI
NSI
(NTT NRM)
DCN or NSI
London
Paris?
Madrid?
Hong Kong
Otemachi
Musashino
Seattle
SC11 Booth
New York
Ingress/Egress point of video stream
Measurement point (NTT’s High-resolution perfSONAR)
Otemachi
New York
DCN or NSI
Osaka

## Slide 8: Path setup signaling
For in case some DCN enabled domains do not support NSI yet in Nov. 2011
  we develop and use NSI-DCN converter
For in case some domains do not interoperate successfully
  we use tree model signaling as well as chain model signaling
  we use chain model signaling for inter-domain path traversing DCN enabled domains
NMS
Manual negotiation
NSI (Tree)
NSI enabled NRM
NSI Client (PCE)
NMS
NMS
Static
(inter-)
Dynamic
(intra-domain)
Dynamic
(intra-domain)
NSI (Chain)
IDCP(Chain)
DCN enabled NRM
NSI-DCN Converter
NSI Client (PCE)
DC
DC
Dynamic
(inter-domain)
Static
(intra-domain)

## Slide 9: Thank you
See you at SC11 NICT Booth #4717